Model:	TAZ 3D Printer Batch
Connect TAZ Printer with it's own power supply to computer.
Turn on Power Supply and Printer
Flashing and testing on a Computer.
- Verify power jumper is correct on RAMBo board
- Add “On” and “Serial Number” stickers to system
- Connect TAZ Printer with it's own power supply to the computer
- Turn on power supply and printer
- Flash printer with default Firmware.
- Verify LCD is working properly
- Connect to printer with Pronter.
- Set Extruder temperature to 230C, if after about 45 seconds the tempature has not changed something is wrong
- Wait for at least 15 seconds after extruder reaches set temperature to continue
- Check extruder Calibration
1. Install 3mm ABS filament
2. Set Extruder springs to 10mm between back of head and latch
3. Mark filament at 100mm and 120mm
4. Extrude 100mm of filament at 70mm/s
5. Measure how much filament was extruded
6. Use equation to calculate new step settings.
7. Disconnect from printer in Pronter
8. Reflash with new step setting
9. Reconnect printer to Pronter
10. Repeat steps 3-5 to check new setting extruded 100mm
 If it does not extruded 100mm repeat steps 6-10 as well
1. After successfully extruding exactly 100mm, double check and extrude another 100mm and measure again
2. Only continue if the printer extrudes 100mm twice in a row.
- Make sure to set Extruder temperature to 230C
- Lulz heated bed with thin film of ABS/Acetone mixture
- Set Bed temperature to 85C, if after about 45 seconds the temperature has not changed something is wrong
- Set motors to off from Pronter
- Check manually that the X and Y switched will activate by slowly sliding the axis.
- For the next steps be careful and have hand near the power switch in case of an error or a crash.
Home X,
If the switch does not activate, stop the printer and check the
wiring or for possible obstructions. Verify 1mm from edge location.
Home Y,
If the switch does not activate, stop the printer and check the
wiring or for possible obstructions. Verify 12.5mm from edge location.
Home Z, Be extremely careful and do not let head crash into bed
     If the switch does not activate stop the printer and check the
wiring or for possible obstructions.
- Rough calibration of bed height, adjust the z height so the nozzle when homing, in Z, just touched the glass in the center.
- Verify that the X Axis rods are near level to the frame. If not Set motors to off and adjust individual z motors
- Print Bed Calibration
- Level bed as need to get a nice bed calibration.
- After bed is level reprint Bed Calibration to verify.
- Disconnect from printer in Pronter
- Turn off printer and power supply
- Disconnect printer from computer, leave power supply connected.
- Unplug power supply from outlet
- Move printer to SD testing area.

Testing SD
- Connect printer power supply to power outlet
- Turn on power supply and printer
- Put Calibration SD card in the slot on the side of the LCD screen
- Using LCD navigate to “Print from SD”
- Select “burnin.gcode” to start the bushing break-in
- Wait for bushing break-in to complete
- Using LCD navigate to “Prepare”
- Select “Preheat ABS”
- Wait for Extruder 1 to reach 230C and Bed to reach 85C
- Using LCD navigate to “Print from SD”
- Select “octo...gcode” to print the test Octopus
- Leave the finished Octopus on the bed until checked by Aleph Objects Quality Control.
- Cut filament 2-3cm above the extruder and leave the filament still in the extruder in place for shipping.
- Using LCD navigate to “Print from SD”
- Select “z_shipping.gcode” to lift z to shipping location
- Remove Calibration SD from side of LCD screen
- Turn off printer and power supply

Wait for approval to continue from A.O. Quality Control

- Remove octopus from bed and leave with its printer for later packaging
- ReLulz the heated bed with thin film of ABS/Acetone mixture
- Attach Electroinics cover with 4x M3 x 13mm bolts and washers