Model:	TAZ 3D Printer
Serial Number:	_______________________
Date Completed:	_______________________
Tested by:	_______________________
Bed Number	_______________________

Configuration:
Electronics:	RAMBo 1.1 with Honeywell thermistors
Firmware:	Marlin 2013-Q3
Nozzle:	Budaschnozzle 2.0a with 0.35mm nozzle
Settings:
motor	steps/mm	max length	microstep mode	digipot
X	100.5	298	16	175
Y	100.5	275	16	175
Z	800	250	4	220
E0		NA	16	135

Test and Verification Results:
- X, Y and Z stop switches verified.
- LCD functions normally
- Drive rod is lubricated
- Belts aligned on bearings and properly tensioned.
- Verify case fan is spinning freely.
- X, Y and Z motion smooth over range and speeds.
- X Home is 1mm from edge of bed
- Y Home is 12.5mm from front of bed
- Cables secure and free of interference/contact with table motion.
- Bed temperature control verified.
- Budaschnozzle temperature control verified.
- Extruder control verified.
- Extruder calibration successful.
- Bearing conditioning complete.
- High speed run-in complete.
- Bed leveled.
- Test print (Octopus) successful.
- Raise Z to top of frame for shipping.