SHENZHEN TONGLIYUAN ELECTRONICS CO., L T D.

S-360W SINGLE OUTPUT SWITCH POWER SERIES

| Characters： ● AC input voltage range choose by switching ● Small volume ,light weight ,high efficiency ● Protecting characteristic: short circuit/overload ● Air cooling ● Provide with starting up display（LED） ● 100% full load burn-in testing ● 2 year quality assurance Size：215X115X50mm Electrical specifications |
| --- |
| Model | S-360-5 | S-360-12 | S-360-24 |
| Output | DC output voltage | 5V | 12V | 24V |
|  | Output voltage tolerance | ±1% | ±1% | ±1% |
|  | Rated output current | 50A | 30A | 15A |
|  | Output current | 0~50A | 0~30A | 0~15A |
|  | Output power | 250W | 360W | 360W |
|  | Ripple and noise | 100mVp-p | 80mVp-p | 80mVp-p |
|  | DC adjustable range | ±10% | ±10% | ±10% |
|  | Setup rise hold up time | 200ms,50ms,20ms |
| Input | Input voltage range | 85～132VAC 170～264VAC 47～63Hz， 240～370VDC |
|  | AC input current | 6.5A/115V 4A/230V |
|  | Efficiency | 74% | 82% | 85% |
|  | AC inrush current | Cold start current 25A/115V 50A/230V |
|  | Leakage current | ＜3.5mA/240VAC |
| Protection characteristic | Over load protection | 105%~135%rated output power start the over load protection |
|  |  | Protection mode : cut off the output，auto-recovery |
|  | Over-voltage protection | 115%-135% cut off the output，auto-recovery |
|  | Over-temp protection | Rectifier≥80℃cut off the output ,auto-recovery |
|  | Fan ON/OFF control | ≥55℃ Fan start ,≤45℃Fan off |
| Environment | Working temperature | -10℃～+60℃;20%～90%RH(please refer to the Load deduction curve) |
| Security | Withstand voltage | Between input and output::1.5KVAC The input and ground : 1.5KVAC The output and ground :0.5KVAC |
|  | Insulation resistance | Between input and output: The input and ground, the output and ground: 100M 0hms /500VDC |
| Others | Weight/Packing | 1.0kg/20PCS/20kg |
| Remark：1..All parameters at the unspecified condition, should be measured in the 230V input voltage ,at the rated load and 25℃。 2. Ripple and noise voltage is measured at the end of 20MHz Bandwidth of oscilloscope ﹑12 inch Twisted pair plus 0.1u and 47u。 3. Tolerance is the sum of voltage setting error、voltage regulation rate and current regulation rate。 |

Physical dimension，Units：mm Terminal Pin feet distribution Pin feet distribution Distribution Pin feet distribution Distribution 9 AC/L 4 6 DC OUTPUT -V 8 AC/N 1 3 DC OUTPUT +V 7 FG