Model:	TAZ 2.1 3D Printer
Serial Number:	_______________________
Date Checked:	_______________________
Checked by:	_______________________
General
- Are all the screws and zip ties tight?
- Are the X and Y axis square to each other?
- Are the gaps at the ends of the extrusion closed?
- Are all the parts flush and straight to the edges with clean lines?
- Are the current version of parts being used?
- Verify that the following are mounted correctly:
    1. Feed tube, tube on back side of mount
    2. Spool Arm, correct height
    3. Double bearing on carriage, step side towards X motor
    4. Finger clip, taller side on left
- Are the switches tight? Do they wiggle side to side?
- Are the switches flush or above the mounts?
- Are all 8 rubber feet installed?
- Is the PET tape free of bubbles and wrinkles?
- Is the heat bed adhesive smooth and consistent with no finger prints?
- Does the extruder mount have 4 unused inserts on the sides?
- Does filament slide through the feed tube?

Y Axis
- Does the Y bed move freely back and forth?
- Is the Y bed tight side to side from motion and twisting?
- Are all the screws on the bearing holders tight?
- Does the Y belt rub the bottom of the y-idler by the bearings?
- Is the Y pulley tight?
- Is one one of the set screws on the Y pulley aligned with the flat on the motor shaft?
- Is the level of the Y pulley at the same height as where the belt mounts on the belt holder?
- Is the Y belt tight?
- Are the bed leveling springs/posts in the correct place?
- Are all the Y mounting brackets flush and tight?
- Are the Y bars approximately 4mm inside of the end plates?
- Are the belts trimmed far enough to not interfere with the pulley or bearing?

X Axis
- Is the X pulley tight?
- Is one one of the set screws on the X pulley aligned with the flat on the motor shaft?
- Is the belt free from rubbing anywhere during motion?
- Is the X belt tight?
- Does the X axis move freely end to end?
- Are the X bars flush with the left side?
- Are the screws that hold the X bars tight?
- Are the belts trimmed far enough to not interfere with the pulley or bearing?

Z Axis
- Is there a washer under the Z adjustment spring
- Is the Z adjuster vertical?
- Are the coupler zip ties tight. Do vertical pull test.
- Are the Z nut holders oriented correctly with the spring under the nut?
- Are the Z bars flush with the top plate?

Extruder
- Can you adjust the extruder springs?
- Are the V grooves on the extruder gears lined up?
- Is the extruder mount secure on the x-carriage?
- Does the idler bearing stick out of the idler block?
- Is the hobbing aligned to the hole in the extruder?
- Is the set screw in the small gear tight and on the flat of the motor shaft?
- Can you feed filament about 115mm from the top of the extruder?
- Are the gears tight with no back-lash?
- Do the extruder gears turn smoothly for several rotations?

Electronics
- Are the screw terminals tight with no insulation inside the clamp?
- Are the RAMBo board, switch and plugs wired correctly?
- Are the quick disconnect terminals pushed all the way onto the switch?
- Can you plug in USB cable from the outside of the enclosure?
- Is the fan mounted on the cover correctly?
- Are the motor extension ground wires secured to the case?
- Is the lower strain relief and cover installed?