TAZ road trip testing notes:

5 TAZ printers in shipping boxes were driven around for a weekend to try and simulate any damage that might be caused by shipping. One of the 5 printers was dropped in box as well.

All 5 printers moved well through the full range of all 3 axes, had no apparent loose, broken or missing parts; belt tension was good. After standard unboxing calibration (detailed below) all 5 printers successfully printed the HQ-octopus test print.

Standard unboxing calibration: This is the calibration that customers are supposed to do upon first setting up their printer; it's detailed in pages 47-56 of the TAZ manual (might vary based on version).

KT-PR0015-6032
- Z- height changed by 2.5-3mm (z adjustment screw went up)
- bed was level
KT-PR0015-6027
- Z height was ~2mm too high (z adjustment screw went up)
- Z was ~1mm higher on the left side than on the right (bed was still level in y)
KT-PR0015-6028
- Z-height was high by .5mm (z-adjustment screw went up)
- bed was level
KT-PR0015-6035
No calibration necessary
KT-PR0015-6031 (dropped)
- Bed level on left side was dead on
- Right side of bed was ~1mm low (noz too high)
  - Seems like the Z axis may have been shifted up on the right side, since the front and back of the bed were at the same height.
KT-PRN0015-6029
- Bed was level and z-height was calibrated well
- nothing broken, missing or out of spec