Guava – Internal Control Box (CB) Harnesses

Harness No	Harness	Description
1	CB_ Power Harness	From 24VDC 4POS Connector receptacle to On/Off switches & black 6POS power terminal block.
2	CB_ Extruder 1 Harness	From 14POS Extruder-1 female receptacle to Rambo X11 connector for nozzle Heat-0 & Fan-0, E0-motor driver connector, T0 thermistor connector, and box ground post.
3	CB_ Extruder 2 Harness	From 14POS Extruder-2 female receptacle to Rambo X11 connector for nozzle Heat-1 & Fan-1, E1-motor driver, T1 thermistor connector, and box ground post.
4	CB_ YZ - Axis Harness	From 14POS YZ female receptacle to Rambo Z-Motor 1, Z-Motor 2 connectors for Right & Left motor drivers, Y-Motor connector, Y-switch(Y-Min) connector, and box ground post.
5	CB_ Xz – Axis Harness	From 14POS X-Axis female receptacle to Rambo X-Motor connector, X-switch(X-Min) connector, Z-switch(Z-Min) connector, and box ground post.
6	CB_ Heat Bed Harness	From 4POS Bed female receptacle to Rambo X11 connector for Heat bed driver connection, and T2 thermistor connector.
7	CB_ LCD Harness	From 25POS female D-Sub connector to Rambo X12 (8-Pin) and X13 (20-Pin) connectors.