AO-Hex Hotend-Subassembly – Juniper and Fangtooth

Required Tools: Torque wrench with 7mm crows foot adaptor, 18mm open end wrench, 4.5mm open end wrench, 1.5mm hex screwdriver, 2mm hex screwdriver, high temperature thread-locking compound

Unscrew heatsink and nozzle – reinstall nozzle using a 7mm torque wrench and holding the heater block with a 18mm wrench. Tighten to 30 in*lbs. Make sure that the nozzle says 5 on the side (0.50mm nozzle).

- Apply thin coat of high temperature threadlock to the entire threaded portion and re-install in the heater block. Install tightly using a 4.5mm wrench and holding the heater block with a 18mm wrench
  - If possible, rotate the heatsink so that one of the points of the heatsink faces the front and the set screw hole is somewhere in the back.
- Lock the threaded extension into the heatsink using an M2x6 SCHS with a small amount of high temperature thread lock.
- Cut thermistor wires to 200mm and crimp on male pins
- Cut the heater cartridge wires to 205mm and crimp on male pins
- Take thermistor and pull back both pieces of the black shielding 1/2”
  - Make sure that the inner clear plastic tubing is all the way down to the bead of the thermistor

Slide ONE of the pieces of black shielding down to the bead of the thermistor and insert into the heater block

- Holding the thermistor leads in place, install the heater cartridge, but do not lock in place yet
- Secure heater cartridge and thermistor into the side of the heat block with a retention plate and an M3x6 BHCS.
  - Be sure that the retention plate is tightened seated completely flush against the block
  - Make sure that the front edge of the plate is parallel to the front face of the heater block.
  - Make sure that the retention plate is covering part of the heater cartridge
  - Make sure that both leads of the thermistor are in the channel in the side of the heater block and not pinched against the flat face. One of the 2 black shield bits should be secured by the retention plate, the other should rest flush with the top of it.

- Pull heater cartridge up against the retention plate and lock into place with am M3x6 set screw from the rear of the heater cartridge.
- Install the heater cartridge wires in pins 1 and 2 of a 4pin connector, and the thermistor wires in pins 3 and 4.

Printhead build
- Build up a hexagon version of the standard TAZ extruder (it will have a hole in the bottom for the top of the hexagon nozzle)
  - Use only black sealed bearings for the extruder
- Mount the hexagon hotend and the extruder on the hexagon extruder mount (It's slightly longer than the one used on the TAZ 4, with a circular cutout for the large gear).
  - Make sure to line up the filament path with an over-sized bit of filament before tightening down.
- Attach a micro blower to the front of the mount with an M2x6 SCHS
  - the micro-blower should have 160mm leads with male pins in a 2-pin housing. The red lead should go in pin 1 and the housing should be marked with blue paint.
- Attach the extrusion fan with shroud to the side of the extruder mount, it's the same exact one we used on the TAZ 4.
- Make sure that all of the wires except for the stepper motor wires are running up between the extruder body and the motor.
- Zip tie all wires into a bundle 1 inch below the connector housings.

Differences from TAZ 4 printhead

- uses hexagon style extruder body (has circular hole in bottom for top of hexagon hotend).
- uses hexagon style extruder mount (has circular cutout for large gear)
- uses black sealed bearings all around
- mini blower with 160mm leads and it's own 2pin connector marked with blue paint

Differences from the Mini printhead
- wire lengths for micro blower, thermistor and heater cartridge all changed
- uses a 0.35mm nozzle for the hexagon hotend
- There isn't a grounding lug on this hotend
- Uses TAZ extruder mount, but same extruder body
- Uses black sealed bearings
- Uses standard 24V TAZ extrusion fan