Belt drive z-axis test outline:

Objectives:
- Determine whether the proposed belt drive system can deliver the same positioning accuracy and low hysteresis as the current screw drive system over the expected lifetime of the system
- Determine whether the belt drive will stretch or degrade in accuracy or precision over time over the expected lifetime of the system
- Determine whether the belt drive poses any danger to the user (eg. The x-azis falling on loss of power)
- Determine the cost of a z-belt drive in quantities to determine of the cost savings are worth the possible downsides

Test 1: Positioning accuracy and longevity (500 hrs – 4 weeks 24/5)
A machine built with the belt drive z-axis should be built and the z-axis run up and down the entire length of the axis continually, with measurements being taken every X number of runs. This data should give us an idea of the accuracy of the system over time

A test for belt tension should be developed, and the tension of the belts recorded every Y number of runs.

Test 2: Positioning precision: (500 hours - 4 weeks 24/5)
To test the precision of the belt drive, a printer should be set up with auto leveling to enable <50um movements along the axis. The machine should repeatedly print test parts that can be analyzed and recorded.
Leveling test: this will give us a good map of the printers ability to level the bed, and measurements along the perimeter will indicate if the resolution of the belt drive is sufficient