Kauri Mechanical Projects

Main Goals of redesign: (1) Autoleveling, (2) Simplified OOB experience, (3) Cheaper, (4) easier to manufacture, (5) larger / cubiv build volume, (6) reduce / eliminate axis droop, (7) easier extruder mechanism

- X-axis
  - Dependent on Y-axis
  - stiffen, either through different linear guides or horizontal rods
  - The y-axis needs to fit around whatever mechanics we have here
- Y-axis
  - Dependent on Z-axis configuration
  - Drop bed if possible
  - Easier installation
- Z-axis
  - Make z-axis easier to manufacture
  - Belt drive in testing, will likely need to pursue parallel paths while we extensively test belt drive system for reliability
  - Dual switch design for z-homing
- Autoleveling
  - Decide on wiper type / location
  - Dual z-min switch for squaring z-axis
  - same basic function as Mini
- Control Box redesign
- Sheet metal redesign
- Mechanical / performance testing
- Profiles
- Design for injection molding

Early prototype / feasibility phase (5/20-6/22)
- Build up and test all proposed changes piecemeal
- run extended lifetime testing on any changes that don't have a 100% confidence level
- Design configuration lock 6/22, Need CAD model of the
Development phase (6/22-7/20):
- Flush out design of all components based on the locked design configuration
- Continue long temp testing of new systems independently
- Begin benchmarking performance

New Systems:
- Z-belt drive
  - geared stepper motors
  - z-upper/lowers
  - dual rod system
- Injection molded parts
- v-slot
- hex blower replacement
- new wiring / cable chain
- TAZ Autoleveling
  - dual z-switch
  - downward homing
- Sheet metal
- Integrated electronics
- LCD redesign / workflow
- modified x-axis
  - horizontal bars
  - tighter bearings
  - different linear guide system
- New board
- New wiring connector scheme
  - try to get rid of 14 pin connectors
  - Need to figure out how the bed will detatch
- extruder redesign
  - reconfigure latch to be easier – more intuitave

Parts that we can start designing for IM now:
- Spool Arm
- Feed tube holder
- Feed tube spinner
- Belt mount (mini style)
- Mini handle (maybe)
- Bed corners (TAZ) – will be rubber / silicone
- Extruder latch???