Design Qualification – Aleph Objects R&D
TAZ 6 Heatsink fan

Summary: In order to qualify the design choice to switch from the 5v microblower to a 5v 40mmx10mm fan, we need to ensure that it does in fact provide better cooling, that it has sufficient lifetime, ando other relevant concerns

Design requirements:

Requirement:	Qualification:
The fan change should result in heatsink temperatures lower than the current 5v microblower	The heatsink temperature must be at least 5% lower across the printable temperature range (180-295C)
The fan should have an adequate lifetime compared to the expected useful life of the printer	We should set up a test fixture to constantly run a fan to verity the mfr. Lifetime spec, and test the fan for at least 1400 power cycles.
The new fan shouldn't make the printer noticeably louder	A TAZ 6 with the new fan shouldn't be any more than 0.5dBa louder than the equivalent TAZ 6 with a microblower fan.
The fan mount must survive shipping	In drop testing, there can be no damage to the fan duct, the fan or any other part of the printer caused by the fan.
The hotend should still be able to maintain 295C with the 5V fan running	The toolhead should be able to heat up to 295C in less than 5 minutes and maintain this temperature to within 5degC over the course of 30 minutes of printing.

Test Procedures:
- Test 1: A heatsink will be fitted with a thermocouple to monitor the internal temperature of the heatsink at approximately the fifth heatsink fin. The printhead will be stepped up from 180 to 290 in 10deg C increments and the maximum heatsink temperature recorded for each temperature. These will be compared between the microblower and 40x10mm fan.
  - Estimated time frame: 1 day
- Test 2: A test fixture should be created to run one fan constantly and to cycle another on and off for 5 seconds at a time. This fixture should be run constantly until either 700hrs / 1400 power cycles have passed without failure or until the failure of one of the 2 fans.
  - Estimated time frame: 1 month

- Test 3: When the first prototype shipping foam arrives, the printers should be drop tested and examined for any damage to the heatsink fan, duct or toolhead caused by the heatsink fan.
  - Estiated time frame: 1 day
- Test 4: With the fan running, the toolhead should be ramped to 295C (the hottest temperature allowed by the firmware), and the time to reach 295C measured (it should be below 5 minutes). During a 30 minute polycarbonate print, the heatsink temperature shouldn't drop below 290C at any point.
  - Estimated time frame: 2 hrs.

Results summary:

Design Qualification Outcome: