Titan -GPLv3 rerelease possible

V3 Hotend wishlist:

- No welds on heat-break, go to single piece similar to MOAR
  - Fine
- Improve heatsink cooling from v2
  - Should be fine
- Higher wattage heater cartridge
  - We can do whatever, but advise not exceeding 30w if aluminium is used.
  - This requirement is to overcome issues with excess cooling from print fans. Sock could be alternative way of getting around this issue.
- Circular heatsink
  - Fine
- Ductless heatsink (fan bolts directly to heatsink)
  - Printed ducts are annoying. IM part might resolve the issues behind this requirement.
  - Some design work needs to happen for a rounded ductless sink
    - Joe has ideas
- Coated nozzle (abrasion resistance and slicker)
  - Can do, propose electro-less nickel as we have that ready to rock. Other slicker coatings possible too.
  - Plated tool steel would be pretty baller - perfectly possible.
- Heater block sleeve (see RRD hexagon, E3D “sock”, printrbot, etc.)
  - Fine -currently in work
- Easier nozzle change (olsen block style?)
  - Off-axis tapped hole in sink for additional screw through block into sink
    - Thermal impact?
- Different / better sealant between heater block and heat break
  - It will be fine. Promise. Cross my heart and hope to die. (sanjay :D )
- Stop possibility of heatbreak unscrewing from heatsink with positive locking.
  - Grub screw? If heatsink is mill-turned with flat side for ductless fan attachment we may be able to sneak in a grub screw.
  - Other?
- Partial PTFE or twinclad plated filament path
  - Ninjaflex present issues with degraded material adhering to internals of hotend, and generally adhesion making printing flexibles a pain.
- 350C
  - Easy, maybe needs a slightly more pimping thermistor.
- 400C
  - Block cannot be aluminium anymore - go copper alloy. Needs not-thermistor sensor.
- 500C
  - Same as 400C
- Incorporate filament drive into heat sink for minimal filament compression zone / less slop
  - Lidsink?- titan add on with integrated filament path
- Incorporate the nozzle into the heat break to eliminate any chances of leaking
  - £$£$ and we haven’t done it before, unknown unknowns, hard. Very hard.
- Clamp style connection between heater block and heat-break and heatsink and heat break for better thermal transfer w/o grease
  - Doable, adds cost.
- Different nozzle tip geometry? (larger flat = better top layers, smaller flat = better dimensional accuracy
  - Plating or polishing probably gets you better top layers for free. Larger flat inadvisable.
- Make narrower toolhead angle for wire-frame printing (no close fans, much lower than carriage)
  - Optional different nozzle/block combo for long reach.
- Easier to swap hotend in and out
  - Non-groovemount solution inbound from E3D
  - Possibly easier way of ejecting heatbreak and everything below.
- Protection of hot parts (other than sleeve)
  - Stainless guard? - Integrated into tool head ala-ultimaker?? UL cert = <200C surface temp
- Pressure feedback / monitoring
  - How much do you want to spend? :D Strain gauge… Encoder wheel?
- Method to stop ooze (needle / ball valve / external stop plate)
  - Maybe for the next version…… :D
- Heater cartridge not sticking out
  - Custom length heater is perfectly possible.
- Cartridge or screw in style heat sensor
  - E3d evaluating now