Title: 2 part bed performance testing
Test Plan: TP-RD00022
Document Date: 04.10.17
Test Date: 04.12.17-05.12.17
Testing Location: Aleph Mountain

This test will be used to determine the expected lifespan of current and prototype print beds. The testing will also asses the longterm wear on the print bed assembly from repeated disassembly and reassembly.

PURPOSE:
The purpose of this test is to determine the lifespan of current and prototype heat beds in a production environment. If the 2 piece bed option being tested performs comparably to the current heat bed setup then we will proceed with development.

RESULTS SUMMARY:
Bed #	Date Installed	Date replaced	Reason for replacement	Notes
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18

CONCLUSION:

TBD.

BACKGROUND INFORMATION:

The current heat bed solution is a 3 part laminate consisting of a borosilicate glass plate layered with PEI on the top side and a heating pad on the other. This solution is extremely effective for most printing applications but it is subject to wear and is extremely costly to replace as the heating element must be replaced along with the glass/PEI laminate. Because of this, the company takes on a large financial burden in the RMA of beds that fail within warranty.

In order to ease these burdens a new 2 piece bed solution has been developed to lower the cost of bed replacement by separating the heating element from the borosilicate plate. This solution also enables easy changing of beds so that the plate can be flipped over to print directly on glass, or any other stick on bed surface on the market.

EQUIPMENT:

30 2-piece heatbed prototypes will be built up using 410 stainless steel (15) and 1075 spring steel (15).

PROCEDURE:

Cluster Testing: 18 2 piece heatbed prototypes will be put into the cluster to compare the performance to the current bed configuration. The beds will be used and maintained in the same fashion as the current cluster beds and should be replaced with new PEI/glass laminates when they reach an unacceptable level of wear as defined by current cluster standards.

In house testing: A set of 6 beds (3 of each material) will be passed around the building to a minimum of 15 people to install on TAZ 6 printers and be tested in more of a standard use case than the cluster testing. Any notes or issues encountered should be recorded and addressed prior to proceeding with development.

TEST DATA and COMPLETE RESULTS:

Bed #	Date put into cluster	Date removed from cluster	Notes
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18

Cluster testing notes and observations:

In house testing notes and observations:

OTHER INFO:

This test plan may not contain all info or data but is to be used as a starting template for a test plan