How to push profile changes to Cura

1. Open the .curaprofile that has the changes you wish to update
2. Open the corresponding file in Projects/cura/build-master/build/dist/resources/ quality/(printer_nozzle)
3. Save as the file from the Projects folder to your desktop
4. Copy over or modify the settings from the .curaprofile with the changes to the file from the Projects folder that is now saved on your desktop
5. Save the changes to the desktop
6. To check that there were no duplicate settings or spelling mistakes, copy the file from your desktop and paste it into the Projects/cura/build-master/build/ dist/resources/quality/(printer_nozzle) folder, when asked to overwrite or replace the file, click “Replace” (not all).
7. In a new terminal, type cd ~/Projects/cura/build-master/ and press enter
8. Now, clear your cache by entering rm -rf ~/.cache/cura-lulzbot ~/.config/cura-lulzbot ~/.local/share/cura-lulzbot
9. Now launch Cura by typing cd build/dist/ in the terminal pressing enter, then typing LD_LIBRARY_PATH=${HOME}/Projects/cura/build-master/build/inst/lib ./cura-lulzbot and pressing enter
10. As long as Cura doesn’t crash, move on to step 11, if Cura does crash, return to step 4 and ensure there are no duplicate settings or spelling errors
11. Open a new terminal and enter cd ~/Projects/cura/cura-lulzbot and press enter
**--make sure you are in the master branch for the pull.
12. Do a git pull to ensure it is up to date
13. Create a branch with the same name as the Ticket with the updated .curaprofiles using git branch T#### and pressing enter
14. Navigate into the new ticket using git checkout T#### and pressing enter
15. Now, copy the updated .cfg files from your desktop and paste them into Projects/cura/cura-lulzbot/resources/quality/(printer_nozzle), replacing when prompted
16. In the terminal, type git commit -a -m “T#### - Updated (material) profiles for (printer)” and press enter
17. To finally push them, type in the terminal git push origin T#### and press enter
18. TO ensure you are back on the master branch after the push type git checkout master and hit enter
18. Now you can reassign the ticket to Alexei and he will review and merge

How to Add Materials to Cura

#. To check that there were no duplicate settings or spelling mistakes, copy the file from your desktop and paste it into the Projects/cura/build-master/build/ dist/resources/quality/(printer_nozzle) folder, when asked to overwrite or replace the file, click “Replace” (not all).
#. In a new terminal, type cd ~/Projects/cura/build-master/ and press enter
#. Now, clear your cache by entering rm -rf ~/.cache/cura-lulzbot ~/.config/cura-lulzbot ~/.local/share/cura-lulzbot
#. Now launch Cura by typing cd build/dist/ in the terminal pressing enter, then typing LD_LIBRARY_PATH=${HOME}/Projects/cura/build-master/build/inst/lib ./cura-lulzbot and pressing enter
#. As long as Cura doesn’t crash, move on to step 11, if Cura does crash, return to step 4 and ensure there are no duplicate settings or spelling errors
#. Open a new terminal and enter cd ~/Projects/cura/cura-lulzbot and press enter
#. Do a git pull to ensure it is up to date
#. Create a branch with the same name as the Ticket with the updated .curaprofiles using git branch T#### and pressing enter
#. Navigate into the new ticket using git checkout T#### and pressing enter
#. Now, copy the updated .cfg files from your desktop and paste them into Projects/cura/cura-lulzbot/resources/quality/(printer_nozzle), replacing when prompted
#. To add the files you must type git add -A and press enter
#. In the terminal, type git commit -a -m “Updated (printer) (material) profiles T####” and press enter
#. To finally push them, type in the terminal git push origin T#### and press enter
#. Now you can reassign the ticket to Alexei and he will review and merge

How to Reclassify Materials

1. Navigate to Projects/Cura/cura-lulzbot/resources/materials/(material you want to reclassify)
2. Open the file using Geany
3. Find the <machine> you wish to change classification for. See this:
<machine>
<machine_identifier product="lulzbot_quiver_evergreen_bagworm"/>
<metadata key="category">Experimental</metadata>
4. Delete the last line “ <metadata key="category">Experimental</metadata>”
5. Save the file and then copy it into build-master so you can test it by clearing cache and then launching Cura.
6. As long as it doesn’t crash, you can create the branch, commit the change, and then push to origin

How to duplicate Profiles

1. Open the file you wish to duplicate
2. Save as to your desktop using the new filename. (High_speed, Standard, High_detail. Remember not to use spaces)
3. On line 3, name = , change to appropriate name, High Detail, Standard, High Speed
4. On line 7, quality_type = , high detail, standard, high speed (use lowercase here)
5. Lines 4 and 9 may need to be changed as well if you are slicing for a new machine or material.
6. Save and Copy the file from your desktop to paste in the correct spot in the build-master folder.
7. Clear cache and launch Cura to make sure it doesn’t crash
8. Now you can Copy and Paste the file into the correct place in the cura-lulzbot folder and commit.
9. Before committing changes, this new file will need to be added with git add <filename> (don’t need the brackets), you can check to see what has been staged with git status. If git add doesn’t work, you can use git add -A to add all. **Make sure you are only committing what you mean to**

Renaming Profiles for New Materials

1. Naming structure should follow this pattern: Type of material_ (Manufacturer)_ProfileSetting_Machine_Toolhead
2. When you have a new material, a file must be made in Projects/cura/build-master/build/dist/resources/materials/ with the supported machines listed under the other info.
3. Open the file that you made changes to to create the new material profile and copy the first 26 or so lines up until the first line that says <machine>. Should look something like this:
<?xml version='1.0' encoding='UTF-8'?>
<fdmmaterial xmlns="http://www.ultimaker.com/material">
  <metadata>
    <name>
      <brand>Generic</brand>
      <material>PLA (IC3D)</material>
      <color>Generic</color>
      <category>Experimental</category>
    </name>
    <GUID>09bb79b8-e516-44fb-b6e5-be165c89c64e</GUID>
    <version>1</version>
    <color_code>#ffc924</color_code>
    <info_link>https://www.lulzbot.com/store/filament/pla-verbatim</info_link>
  </metadata>
  <properties>
    <density>1.25</density>
    <diameter>2.85</diameter>
  </properties>
  <settings>
    <setting key="print temperature">205</setting>
    <setting key="heated bed temperature">60</setting>
    <setting key="standby temperature">175</setting>
    <setting key="soften temperature">140</setting>
    <setting key="probe temperature">140</setting>
    <setting key="wipe temperature">140</setting>
    <setting key="part removal temperature">45</setting>
4. Copy those lines over to your new material file and change the material name to reflect the new material and manufacturer in parenthesis.
5. Now you can add all of the machines and toolheads that you have developed for the new material after the last line. Should be in the following format:
 <machine>
      <machine_identifier product="lulzbot_taz6_cecropia"/>
    </machine>
    <machine>
      <machine_identifier product="lulzbot_hibiscus"/>
    </machine>
6. Make sure after the last supported machine, the lines:
</settings>
</fdmmaterial>
are present.
7. Once the file is finished, make sure to save it and then clear your cache and test to make sure everything is correct by using steps 7-10 of How to push profile changes to Cura.
8. Now you can update your profiles from the previous material you used to make the profile, just remember to change both the file name to reflect the new material, and the “material =” line under [metadata] in the first few lines of the inst.cfg file

How to Add Toolheads to Old Printers

Changing a printer definition:
1. Open one of the printer definitions of the printer you are trying to add the toolhead to, under /home/aleph/Projects/cura/build-master/build/dist/resources/definitions/
2. Save it to your desktop with the current toolhead in the file name replaced with the new toolhead name.
3. Now open the file using Geany and change any line that references the toolhead. Such as the “id” : line, “name”: line, “0”: line, “preferred quality”: line should be “*Standard*” usually, the “machine name”: line, the “firmware_toolhead_name”: line, the “user_toolhead_name”: line, and the start gcode line.
4. Save the changes to your desktop.

Creating an extruder definition:
1. Open the extruder definition of the machine you already have one for and save it to your desktop with the new file name reflecting the proper machine that you just updated the printer definition for, under /home/aleph/Projects/cura/build-master/build/dist/resources/extruders/
2. Open the new file from your desktop using Geany.
3. Lines 2 and 7 will need to be updated to reflect the correct new printer.
For example changing "id": "lulzbot_redgum_goldenrod_extruder" to "id": "lulzbot_hibiscus_goldenrod_extruder" doing the same with the “machine”: line.
4. Save your changes to your desktop.

Duplicating and updating the Start Gcode:
1. Open the start gcode for the new printer under /home/aleph/Projects/cura/build-master/build/dist/resources/gcodes/
2. The file should be saved to your desktop and renamed according to what you called it in step 3 of Changing a printer definition.
3. The first line needs to be changed to reflect the correct toolhead, according to the following format: lulzbot_(printer dev name)_(tool head name)_(start/end). An example: This G-Code has been generated specifically for the LulzBot Mini 2 with HE 0.5mm Tool Head

Adding the printer to the different material types
1. Since you have already created the profiles for the new toolhead on the new machine for multiple different materials, those materials need to be updated to support the new toolhead on the old machines. Make sure you have a list of these materials so you only do the ones that you have profiles for.
2. Starting with the first material on the list, open it up using Geany under /home/aleph/Projects/cura/build-master/build/dist/resources/materials/
3. Save as that file to your desktop.
4. Scroll down through the supported machines until you find the printer that you are adding the new toolhead to.
5. Using the following format (without parenthesis), add the new printer to the material file:
 <machine>
      <machine_identifier product="lulzbot_(printer)_(toolhead)"/>
    </machine>
For example I was adding the goldenrod toolhead to the hibiscus printer with:
<machine>
      <machine_identifier product="lulzbot_hibiscus_goldenrod"/>
    </machine>
For all the supported materials.
6. Save the file to your desktop and do the same thing with the next material on the list, saving all the files in the same place.

At this point, copy all of your files back into where they came from and clear your cache and launch cura from your terminal using steps 7-10 of How to Push Profile Changes to Cura to see if it crashes. If not, you are good to start the next step.

Duplicating profiles for the new Toolhead on the Old machines
1. Open a new terminal and enter cd ~/Projects/cura/cura-lulzbot and press enter
2. Do a git pull to ensure it is up to date
3. Copy the folder holding all of the Profiles for the original machine and toolhead to your desktop in the same place that all of your other files have been saving to.
4. Rename the folder to replace the current machine with the new one.
5. Open a new terminal and Change directory (cd) to the folder you just renamed (should be in your desktop).
6. Once in that folder in the terminal, enter the command line:
rename 's/<old name>/<new name>/g' *
For example: rename 's/redgum_goldenrod/hibsicus_goldenrod/g' *
7. Then to search within the file and update automatically, enter:
sed -i 's/<old name>/<new name>/g' *
For example: sed -i 's/redgum_goldenrod/hibiscus_goldenrod/g' *
**Keep in mind there is a space between the last ‘ and *
8. Now copy that entire folder to drop it back into the build-master folder you got it from and run cura to test again using steps 7-10 of How to Push Profile Changes to Cura.
9. While in cura, verify that the correct toolhead is now available on the correct machine, and that all the profiles are available. Also check to see if the wiping location at the start of the print is correct, to do this, make sure your printer is flashed to the correct firmware (most recent stable one) and has the correct toolhead mounted.
10. Once you check to make sure everything looks right, drop all of the files into the correct places in the cura-lulzbot folder and commit and push all of your changes to the branch labeled with the ticket number as you would in steps 11-18 in How to Push Profile Changes to Cura.
10. Remember: If you need to change a profile for the toolhead you just updated old printers for, it needs to be updated for all the printers as well! Easy to do with the steps outlined above (duplicate profiles folder for other printers).