Saniwave Filament testing notes:

Notes:
- The PLA contains a small amount of TPU, making it stickier when melted and less brittle than standard PLA.
- ABS came in nice looking colors, produced strong parts
- All filament was actually a bit more consistent than Village Plastic's filament (avg variance of 0.04mm), but was slightly larger (Village's filament tends to be 2.85 +/- 0.04mm, this tends to be 2.97 +/- 0.03mm). Might not seem like a lot but this will cause a well calibrated machine to over extrude by ~7% on average. We can compensate in the slic3r configuration, but will need to have a separate config for this plastic.
- Seemed to droop slightly more than standard PLA (see Brent I's Pi jar print), could fix with more time spent on configuration

Recommendation: I really liked the PLA, it prints easily and makes slightly stronger parts than standard PLA. I think that the difference in diameter of filament is a bit of a deal breaker if we want to supplement our existing ABS and PLA filament as 2 ABS/PLA config's would be messy. We could hype that the PLA is mixed with TPU and sell it as a separate material with it's own configuration, I think people would love it (and it's way cheap). We could also contact and see if they can try to make us slightly smaller diameter filament.

Filament diameter accuracy / consistency:
Filament	Variance in diameter	Maximum out of round	Extrusion temperature
Natural PLA	2.93-3.01 (0.08mm)	0.05mm (2.96-3.01)	150C-200C (185 ideal)
Black PLA	2.96-3.01 (0.05mm)	0.06mm (2.95-3.01)	165-210 (200C ideal)
Yellow PLA	2.92-2.98 (0.06mm)	0.05mm (2.92-2.97)	150-200C (180C ideal)

Green ABS	2.93-2.99 (0.06mm)	0.04 mm (2.94-2.98)	215-240C (230C ideal)
Blue ABS	2.95-2.99 (0.04mm)	0.03mm (2.95-2.98)	210-240C (230C ideal)
Orange ABS	2.97-3.00 (0.03mm)	0.03mm (2.97-3.00)	210-240C (230C ideal)

Average	2.97mm +/- 0.03	0.043mm