Hotend testing :

Notes:
E3D
- Sub assemblies
  - thermistor & wires (1)
  - fan & shroud (1)
  - all together
- thick heater wire sucks to crimp to
- thinner (OD) PTFE tubing might be better for thermistor
- Thermistor as a sub assembly is easier to install – use ferrules to keep sleeving right up to thermistor.
- Need to check resistance of thermistor after assembly!! It can easily short to the heater block
- phillips head wood screws are really hart to screw in w/o stripping. SCHS would be much easier; M3x16 wours well but can crack fan shroud.
- Using Kapton tape to secure PTFE tubes over the exposed ferrules – taping to the heater wires for strain relief.
- Push thermistor and sleeving INTO hole before bending or securing
Hex
figure out connector

Assembly
Hotend / Assembler	Time to assemble fully	Notes
E3D 1 / bam	32:30	Thermistor wires shorted on first try, got it the 2nd try
E3D 2 / bam	26:25	Easier to assemble
E3D 3 / bam	22:47	Getting better. Cracked the fan shroud using M3 x 16 bolts, would not happen if not over tightened
E3D 4 / bam	21:27	All went well
E3D 5 / bam	22:43	All went well

Hex 1 / bam	5:39	Still need new fan mount, add time to assemble that to <---
Hex 2 / bam	2:54
Hex 3 / bam
Hex 4 / bam
Hex 5 / bam