Print Octopus
Measure skirt, Range is 0.30mm to 0.45mm
Double check mechanical, screws couplers etc.
If outside range:
M851	-	Verify offset is 1.43
Based on measurements shoot for a .38 squish
Over-squish: .38 – measurement = X. Then: 1.43 – X = Offset
Under-squish: measurement - .38 = Y. Then: Y + 1.43 = Offset
M851 Z-Offset	-	This will write the new Offset
M500	-	This will save the new Offset
M851	-	This is to verify the new Offset
Print Octopus
Measure skirt
If not in range, repeat
If in range, note new Z offset on Quality Assurance Record