Install guide for Mini two-piece bed

1.) You just upgraded your LulzBot desktop 3D printer with the two-piece bed. After following this quick start guide, your lulzbot TAZ 3D printer will be more capable then ever. Let’s get started!

2.) Included materials:
Lulzbot Mini PEI Modular Print Surface(KT-HB0010), 6 Mil Heavy Duty Poly Tubing Roll - 14" x 500'(SH-PA0052), Mini Heat Bed: 12-1/8 x 12-1/8 x 1/2 44ECT B Brown Die Cut One Piece Folder(SH-BX0074), Mini Heat Bed: 16 x 16 Die Cut Pad (insert)(SH-PA0047), Disposable Desiccant Bag, Silica Gel, for 24 Cubic Inches(SH-PG0099), Mini PEI Modular Print Surface(AS-HB0001)

Lulzbot Mini Modular Heated Print Bed(KT-HB0011),Mini Heater assem from TEMPCO 109 Watt 24V with felt(AS-HB0001), Mini Heat Bed: 12-1/8 x 12-1/8 x 1/2 44ECT B Brown Die Cut One Piece Folder(SH-BX0074), Mini Heat Bed: 16 x 16 Die Cut Pad (insert)(SH-PA0047), Mini Modular Bed Corners Kit(AS-PK0021)

3.) Items required: Metric hex drivers 2MM, LulzBot Mini, Lulzbot Mini PEI Modular Print Surface(KT-HB0010),Lulzbot Mini Modular Heated Print Bed(KT-HB0011)

4.) Turn off your Lulzbot Mini 3D printer.

5.) Unclip the heater bed & heater thermistor wires from the Bed clip, then disconnect both wires (Purple and yellow)from the Heat bed cable harness(Black wires & white/yellow).

6.) Using your 2MM hex driver, Remove the old four screws, washers, and spacers. Please set washers aside

7.) Remove the old heatbed (AS-PR0079), then remove all four flexy corners. Please keep screws, screws will need to be re-used.

8.)Proceed to open box (KT-HB0011) with the Mini Modular Bed Corners Kit(AS-PK0021) which lnclude 4 (PP-GP0296)Flexy Bed Corner, 4 (HD-MS0287) 8mmOD 10MM length unthreaded spacer, 4 (HD-BT0082) Flat head socket cap screw M3, 16 MM, .50MM pitch.

9.)Place each flexy corner on the bed plate and screw in with 2 button-head screws loosely, tighting will be done later.

10.) Place Lulzbot Mini Modular Heated Print Bed(KT-HB0011) onto all four flexy corners, once fitted on top. Please snug tight flexy corners, Do not over tighten

11.)Place the 8MM unthreaded spacer into each flexy corner

12.)Proceed to open box Lulzbot Mini PEI Modular Print Surface(KT-HB0010) Please be careful as glass will be sharp!

13.) First, place your heat spreader on the Mini bed plate.

13A.) Next, place the glass on top of the heat spreader. (Note:PEI side should be up, with smooth glass contacting the heat spreader.)

13B.) Then, using the new spacers. Place a spacer in each in the Flexy bed corner, followed by a washer and M3x16MM screw.

13C.)If using a torque driver, 5 in LB is the max. any more torque can strip the bed plate.

14.) Connect the Heater bed wire(white) to the Heat bed harness wire(black), next connect the heater thermistor(red) to the Bed harness thermistor(white/yellow). And then snap back into the bed clip.

15.) Congratulations, you are done!