Yellow	check for phrasing
Green	Valid for Mini
Red	No longer needed
Pink	non-print notes

Ignore capitalization for now, as most of the non-body guide is in caps.

Page 1- Quick Start Guide
# Setting up your Mini 3D printer

All unpacking related items will no longer be in the guide. The foam pieces will have labels/instructions.

Greenbox:
## Remove Protective Pieces!
Make sure all foam packaging has been removed from the 3D printer. Save all packing materials, packing clips, inserts, documents, and the box in case you need to transport your printer.

 [IMG] Mini, with all packing materials removed.

# 1. __READ THE USER MANUAL COMPLETELY BEFORE POWERING UP YOUR Mini 3D PRINTER__

[URL](lulzbot.com/support/downloads/mini_user_manual)

# 2. Place the Mini 3D Printer on a flat and level surface.

[IMG] Mini on workspace.

# 3 Before printing, familiarize yourself with the Mini
## 3.1 Axes Identification

[IMG] Mini, XYZ photo

## 3.2 Mini components

[IMG] Mini components labeled: (hot end, extruder, heated bed, stepper motors, electronics enclosure, etc)

# 4. Locate the AC power cable and plug the trapezoidal plug into the AC input on the rear of the printer.

# 5. Locate the USB plug on the front of the TAZ electronics enclosure. Plug in the USB cable, square B plug end, into the USB receptacle on the front of the electronics enclosure. Plug the A end of the USB cable into your computer.
[IMG] USB plugged in
#6. Install software and drivers
[Greenbox]: Windows users will need to install the driver. Mac and Linux users will not. Follow the guide found here: [https://ohai-kit.alephobjects.com/workflow/windows-drivers/](https://ohai-kit.alephobjects.com/workflow/windows-drivers/)This may not be needed, as the drivers may be installed during the Cura installation process...

6.1 ## Download Cura Installer
[LINK](/support/Cura landing page)

6.2 ## Launch installer

7. # Setup Cura
[URL] (OHAI-Kit [Cura overview] OR Cura Manual)

7.1 ## Launch Cura!
  - A. First Run Wizard (recommended settings in bold) Select your language: __English__ > Next

                  - C. Select your machine: __Lulzbot Mini__ > Next

  - D. The wizard should now say “Lulzbot TAZ/Mini Cura is now ready to be used with your Lulzbot.”

7.2 ## Setup Print
A. Select __Fast, low quality print__

B. Choose PLA, ABS or HIPS depending on the material you will be using.

8. #Print your first octopus!
[IMG] Printed octopus

8.1 ## Load the octopus model file in Cura
A. Press the __Load File__ icon

B. ## Select the file __Octopus.stl__Change file name to match what's on flash drive

Greenbox: Your first octopus can be found on the flash drive at: Path > to > file > location

9. # View Model
[Greenbox]:
For faster results Cura will automatically slice the model in the background or after any change.

10. # Print your first Octopus
- A. Select __File__ then __Print__ or press the __Print__ button
- B. Pronterface UI
10.1 # Familiarize yourself with the Printing Interface
[IMG] Labeled Screenshot showing Cura print/pronterface UI

10.2 # Remove test filament
- A. Lift up on the two screws on the extruder.
- B. Lower the hinged idler
  [IMG]image showing the above[/IMG]
10.3 # Turn on hot end
Turn on hot end to 230C. This will allow you easily remove the ABS filament used in our testing process.
[IMG]Labeled image showing the hot end and bed controls[/IMG]
10.4 # Remove filament
Once at 230C, pull out the existing filament by lifting up on the sample. If you will be printing with PLA you will need to set the temperature to 180C after removing the existing filament.
10.5 # Load filament
- A. If you have not already done so, rotate up the filament arm (filament holder?) and lock into place.
  [IMG]image showing the above[/IMG]
- B. Place the filament on the filament arm, making sure the filament can unreel down towards the center of the printer.
  [IMG]image showing the above, with the filament path highlighted/noted[/IMG]
  Greenbox: Make sure that the filament end is clear of any debris or adhesive.
- C. Insert the filament end into the hot end.
- D. The filament should travel approximately 4” into the hot end melting chamber.

10.6 # Raise the hinged idler into place, so that the bearing is putting pressure on the filament.
[IMG]image showing placing the hinged idler in place[/IMG]
10.7 # While pinching the thumb plate at the top of the two thumb screws lower the 2 screws over the hinged idler
[IMG]image showing the above[/IMG]
10.8 # Adjust idler tension. The two screws should be finger tight
[IMG]image showing the above[/IMG]
10.9 # Test Extrusion
- A. With the hot end at the proper temperature of your filament, press the Extrude 10 button.
  [IMG]Labeled image showing the Extrusion controls[/IMG]
- B. If the hot end has not extruded any filament, tighten the two screws 1 full turn.
  [IMG]Labeled image showing the Extruder screws[/IMG]
- C. Press the Extrude 10 button while pushing the filament into the hot end.
- D. Repeat the above two steps as needed until extrusion is repeatable and reliable.
  [IMG]image showing extruded filament[/IMG]
- H. Remove extruded filament

11 # Bed Prep Are we going to recommend anything for bed treatment with the PEI surface?
The LulzBot Mini 3D printer has a PEI print surface. Make sure that the bed is clean by wiping it clean between prints.

12 # Print your Octopus
12.1 # Press Print
[IMG]image showing the octopus printing[/IMG]
13. # Watch your print

14. # Part Removal

A. After the part is finished, the hot end and heated bed will automatically cool down. When the bed has cooled sufficiantly the bed will move forward to make print removal easy.
[IMG] Printed octo[/img]

- B. Once the bed cools, pop the part off by lifting gently on the part. Are we shipping a clam knife? If so the text may need to read: B. Once the bed cools, pop the part off by lifting gently under the part with the included blue handled knife.
[IMG]image showing the above[/IMG]
[IMG] Octo removed

Greenbox:
Ready to get started? More information and tips can be found in our forums!
[forum.lulzbot.com](forum.lulzbot.com)