Mini-RAMBo
- New fuse holders and fuses
- USB is good
- Design Spin for fuses

Fans
- Need to change 80mm and 40mm fans
- Check on UL for blower

Safety Case is needed
- Does not need to be Fire enclosure
- Finger accessibility test to moving parts and hot parts
- Closed bottom
- Does not need a shutoff switch on door
- Electronics case is to as is for fire enclosure
- Design change
- Possible idea for leaving the printer similar to what it is now but adding to holes covers and a clear vacuum formed “bubble” door on front and back to add depth for the Y axis

Fire rated parts
- All parts inside electronics enclosure must be V-2
- All parts outside electronics enclosure must be HB

Certify printed parts as fire rated
- This is the only way we'll be able to use printed parts on the system
- This will be a separate project from UL
- We don't know currently if they are good or not, may need to change anyway
- We do know the pellets that Village starts with are HB rated. We may just have to certify the process.
- Another project of unknown length

Part #/Serial #
- The Part # must be permanent
- We can split the two numbers or use a UL rated sticker

Wires
- Ground wire must be green with yellow stripe

Heat shrink/EMC shield
- Not currently recognized
- We need to see if we need it
- We'll need to change if we do need it

EMC testing
- Will need to re-test EMC based on changes