Title: TAZ6 Z Mosfet Chip Temperature
Test Plan: TP-RD-00015
Document Date: 08.18.16
Test Dates: 08.12.16-08.29.16
Testing Location: R & D Lab, Electrical Room

PURPOSE:

The end goal of this test is to determine if the Z mosfet requires a heat sink to keep it within operating temperatures defined by the operating specification.

RESULTS SUMMARY:

Test 1: Average With and without HS

Ambient T (ºC)	Heat Sink	No Heat Sink
25		65
26	69.25	66.8
38	56.8
39		57
40	57.3	60.3
41		59.4
42	58	60.6

Test 2: Average temperatures of chip, internal temps and ambient temps

Internal Chassis T (ºC)	Z Chip T (ºC)	Ambient T (ºC)
34.8	44.3	32
36	47.7	32
36.3	49	33
37	48.3	33
37.8	49	34
45.3	56.7	41

Average Temperatures

Chassis Internal (ºC)	PS Internal T (ºC)	Ambient (ºC)
35.1	29.8	30
36.5	30.5	31
38.7	31.5	32
43.7	35	34
47.2	37	36
47.2	37.5	37
48.1	40.2	41

PROCESS:

All tests were performed using multiple TAZ 6 printers in a Light World enclosure. This was to ensure that the environment could be closer controlled without drafts. The units were run using a gcode titled ‘Z_tester’ that would ensure the z axis was moving at all times, creating worst case conditions for the z chip. During the higher ambient tests, the heat bed was turned on at a high temperature which elevated the ambient temps. With this setup, max ambient temperature observed were 42°C. Results from higher temperatures may be interpolated from this data.

The thermal couple was placed on the z chip, routed through the chassis and out through the corner of the enclosure. During some of the tests, a thermocouple Thermal tape was used to ensure the thermocouple stayed in location.

Temperature readings were taken during the course of operation and noted. Test were completed as follows:

Test 1: First test was to evaluate TAZ 6 thermals with heat sink and without heat sink at close to ambient and at an elevated ambient.
Test 2: Evaluate the range of temperatures with no heat sink present. Run the unit from an ambient temperature of 23°C to as high as achievable in the enclosure. From this data we can interpolate what the chip temperatures will reach at even higher temperatures.

EQUIPMENT:

TAZ 6 units: Nutwort 05, Nutwort 19 and Production Unit #30
AcuRite Room thermometer
Fluke 179 RMS Multi Meter
Fluke Type K Thermocouple
Lite World Enclosure

CONCLUSION:

Observations conclude that at low temperatures, the chip temperature can rise quickly but that once the ambient temperature in the chassis raises, the fan on the power supply increases flows, improving the temperatures of the chip.

Based on Test 1, there is little to no difference in chip temperatures with and without the heat sink. The slight difference is within experimental error.

Based on further tests, at 43ºC the maximum chip temperature observed was averaged at 60.9ºC. A delta of 17.9ºC over ambient. Average rise over ambient along all temperature ranges was 24.87ºC, with the maximum rise to be 44.8º C, observed at lower ambient prior to power supply fan increase.

A pass is defined where the chip is able to maintain functionality which is determined by the Operating Ambient Temperatures and the Maximum Junction Temperatures defined in the manufacturers specifications. At an internal power supply temperature of 50ºC, the power supply fan increases its speed, providing additional airflow over the chip in question. Due to this, the z chip temperature goes down slightly or stays the same when the ambient temperature rises.

The manufacturers specification for the chip indicates an operating ambient temperature not to exceed 85°C(185ºF). Interpolating data, the internal temperature of the electronics chassis will be approximately 85ºC at an environmental temperature of 96ºC(204.8ºF). At an internal ambient temperature of 96ºC, the expected chip temperature would be 140.8ºC at maximum observed rises, within the maximum chip temperature.

The z chip based on the data acquired does not appear to need the heat sink. It is well within the range for ambient and for junction temperature as defined by the manufacturer.

RECOMMENDATIONS:

Recommendations are to ship the product without the use of a heat sink on the z chip. Recommend the user does not exceed an ambient temperature of 75ºC (167ºF) to ensure a higher factor of safety.

BACKGROUND INFORMATION:

Chip specifications:
Operating Ambient Temperatures: -20 to 85°C
Maximum Junction Temperature: 150°C
Storage Temperature: -55 to 150°C

Power Supply Specifications state the following:
RTH2≧50°C±10°C#Fan on ; RTH2≦40°C±10°C Fan off (Fan always on for 3.3~5V,Fan ON/OFF
control for 12~48V)

Full component specifications can be found in the following directory and file:
/home/aleph/shared-j/Documents/R&D/Spec Sheets/A4982-Datasheet.pdf

Power Supply Specification can be found in the following:
/home/aleph/shared-j/Documents/R&D/Spec Sheets/RSP-500-spec_taz6_pwr_supply.pdf