Wiper Pad Manufacturing	Standard Operating Procedure

Preparation and Safety:
- Select an area no less than 100' from any structure and spark/ignition source for the work bench. Clear an area no less than 30' on all sides of the work bench of any flammable material, debris, dry vegetation and traffic. Place cones or other clear visual marker to mark the cleared area.
- Identify and remove all sources of spark, flame, lighters, e-cigarettes, etc. from the area.
- Ensure that no vehicle can approach within 100'. Place additional cones if necessary to keep vehicles from the area.
- Place an “ABC” rated fire extinguisher in a clear and visible area about 25 feet from the bench.
- Wear chemical rated gloves when handling acetone.
- Wear safety glasses at all times within 30' of the work bench.
- Perform all Wiper Pad work at the work bench.
Step 1: Prepare the ABS/Acetone Slurry:
- In a 1 or 5-gallon container of acetone, begin by removing a small amount of the acetone from the container to make room for the ABS. This may be added to production stock (acetone is used to prepare glass for heatpad application) or disposed of properly.
- Cut a stock of eSun Black ABS into ~2' lengths.
- Weigh out and mix in 124g of ABS strands per gallon of Acetone. Allow the acetone to dissolve the ABS over 24 hours, or 4 hours with regular hand stirring. Never use a power tool near acetone.
Step 2: Prepare the wiper pad rolls
- Using the slitting jig, slice all 50' rolls of polyester felt into 2 1/2” x50' strips. Be sure to use a fresh razor blade for every 30 rolls or so to ensure a consistent cut.
- Cut each of the felt rolls in half to make 4 25' rolls from every stock 50' roll.
- Roll these tightly on a table to ensure that they are as flat as possible, this will be important to ensure consistent acetone soaking.
- Zip tie the end of each roll to ensure that it stays tightly wound during soaking. Cut off the remainder of the zip tie.
Step 3: Soak the felt rolls in the ABS acetone slurry.
- Perform this procedure in a well ventilated and secluded area (such as outside). Be sure to wear gloves when handling acetone.
- Ensure steel pan has been completely cleaned from previous use.
- Mix abs/acetone container with stick so that mixture is even when poured.
- Fill a 2'x3' stainless steel pan to 1/2” with the ABS / Acetone slurry.
- Quickly drop the rolls completely flat into the mixture. The goal is to completely soak each side of the roll without letting the acetone slurry soak all the way through. This may take several dips but try to avoid letting the roll soak for more than 1 second at any given time.
- When both sides of the rolls are coated, hang them to dry on the rail over the soaking tray so that and excess acetone drips back into the tray. Once the rolls have stopped dripping, they may be transferred to a secondary drying rack to make room for more rolls.
- Check on the rolls and rotate them every hour or so until they are completely dry.
Step 4: Cut up the rolls into individual pads
- Remove the outer and inner rolls of felt that have been completely soaked.
- Using the wiper pad cutting jig (PP-PG0XXX) and a pair of scissors, cut the pads into 90mm sections and package them for distribution (5 to a bag, one additional with each Mini)
Cleanup:
Acetone container(s) must either be sealed or left open to air dry and relocated to the designated trash area.
- Leave all other materials at the work bench until completely dry.
- Re-pack all materials securely.