1.0	Client Information

| Client Information |
| --- |
| Manufacturer Name | Aleph Objects Inc. |
| Address | 626 West 66th Street |
| City | Loveland |
| State | CO |
| Zip Code | 80538 |
| Client Representative | Seth Sinnema |
| Title | CTO |
| Phone | (970) 377-1111 Ext. 644 |
| Fax |  |
| Email | seth@lulzbot.com |

2.0	Product Information - General

| Product Information |  |
| --- | --- |
| Product Name (as it should appear on test report) | TAZ 4.1 3D Printer |
| Model Number (of UUT to be tested) | KT-PR0016 |
| Functional description of product (what is it, what does it do, etc.) | Creates 3D objects from CAD files by melting plastic and drawing the part layer by layer. |
| List all modes of operation | Warm Up and Printing |
| Can modes be operated simultaneously? If so, explain. | No |
| What mode(s) will be used for testing? | Printing |
| Product type (IT, Medical, Scientific, Industrial, etc.) | Commercial and residential |
| Is the product an intentional radiator | No |
| Product Dimensions | 755mm x 520mm x 665mm |
| Product Weight | 12.5kg (27.6lb) |
| Will fork lift be required | No |
| Applicable Standards, if known |  |
| Describe all environment(s) where product will be used (residential, commercial, industrial, etc.) | Indoors, usually office space |
| Does product consist of multiple components? (If yes, please describe each system component) | Yes, Main Printer unit and the Power supply |
| Cycle time > 3 seconds? (If yes, how long?) | Yes, varies based on the size and quality of the part |
| Highest internally generated frequency | 16mhz |
| Product Set-up Time | Less than 30 min |
| Boot up time in the event of an unintentional power down | Less than 10 min |
| Identify ALL I/O connections on the unit(s) under test, as well as MAXIMUM associated cable lengths below |
| Model No. | Description | I/O Type | Length (m) | Patient Connect? (See Note) | QTY |
|  |  | UUT-UUT | UUT - SE |  |  |  |
| ---- | 12VDC Power cord from P.S. to Printer | DC |  | 1.00 |  | 1 |
| 5279 | US 18AWG Power Cord C13/NEMA5-15 for P.S. | AC |  | 1.83 |  | 1 |
| 7692 | EU 18AWG Power Cord C13/CEE 7/7 for P.S. | AC |  | 1.83 |  | 1 |
| 7691 | UK 18AWG Power Cord C13/BS163 for P.S. | AC |  | 1.83 |  | 1 |
| Note: “Patient Connect” column applies only to medical devices. |

3.0	Power

| Power Requirements |
| --- |
| Does/can product connect to AC mains? (If so, can the UUT function when connected to AC?) | Yes, it must be connected to the mains |
| Input Voltage Rating as it appears on unit, power supply, or power brick | 110 or 220 selectable by switch |
| Input Current (specify @ 230 Vac/50 Hz) | 5Amp @ 110-120VAC 50/60hz |
| Single or Multi-Phase (If multi-phase, specify delta or wye) | Single phase |
| Is input power connector two-prong (Hot & Neutral) or 3-prong (H, N, Ground) | 3-prong |
| Does UUT have more than 1 power cord? (If yes, explain.) | Yes, different power cords can be used for plugs in other countries. |

4.0	Unit Under Test (UUT) – Detailed Information

| UUT Hardware |
| --- |
| Condition | On and printing with a 0.35mm nozzle |
| Configuration During Test | Printing test gcode file off of SD card in printer |
| Input Power | 110Vac @ 60hz and 220Vac @ 50hz |
| UUT Components |  |
| Name | Model No. | Serial No. | Description |
| TAZ | KT-PR0016 | KT-PR0016-6616 | TAZ 4.1 3D Printer |
| P.S. | PC-240167 | N/A | 400W 24Vdc Power Supply |
| I/O Cabling |
| See Section 2.0 for details |
| UUT Software/Firmware |
| Name | Version/Revision | Functionality |
| Marlin | 2014Q3_rA | On board firmware for printer control and gcode interpretation |
| UUT Operating Conditions |
| List all frequencies generated/used by the product. | Does not intentionally generate any set frequencies. The frequencies that are produced depend on file being printed and print speed. |
| How will product be exercised during test? | Printing test gcode with ABS filament |
| How will product be monitored during test? | Visually to to make sure printer is continuing to print successfully |
| What are the product’s critical parameters? | Nozzle Temp = 230°C, Bed Temp = 100°C, Print is acceptable |
| Specify tolerance of all critical parameters. | Nozzle Temp ± 4°C, Bed Temp ± 4°C, Print has no visual skips or steps. Printer continues to run throughout testing. |

5.0	Support Equipment (SE) – Detailed Information

| Support Equipment (SE) |  |
| --- | --- |
| Name | Model No. | Serial No. | Description |
| N/A |  |  |  |
| SE I/O Cabling |
| Model No. | Description | Shielded? | Length | Quantity |
| N/A |  |  |  |  |
| SE Software/Firmware |
| Name | Version/Revision | Functionality |
| N/A |  |  |

6.0	Block Diagram

Important note:  The product data sheet is a critical piece of documentation which is used as the basis for any test reports that EMCI will generate; it must be completed prior to testing.  It should be reviewed carefully by the client.  If incorrect information is provided resulting in revisions to test reports, the client will be subject to report revision fees.