Title: TAZ 5 Juniperbush AS/NZ CISPR22:2010(?) Class A Testing
Test Plan: TP-RD-00009
Document Date: 11.23.15
Test Date: 11.20.15
Testing Location: EMI Test Lab LLC

PURPOSE:

Achieve AS/NZ CISPR22:2010 Class A compliance for AC mains conducted emissions and enclosure radiated emissions.

RESULTS SUMMARY:

During the examination on Friday November 20, 2015, the Juniperbush machine passed AS/NZ CISPR22:2010 Class A by a margin of 3.7dBμV/m with 149.35MHz being the closest to the limit; the second closest was 191.98MHz which had a 9.0dBμV/m margin. No changes needed to be made to the machine in order to pass the requirements. The machine was tested when printing both from an SD card (SPI) and from a computer (serial).
CONCLUSION:

The data gathered during the testing of the TAZ 5 Juniperbush machine show that the machine passes the AS/NZ CISPR22:2010 Class A requirements without any modifications. Not including other requirements such as labeling, record-keeping, and other paperwork; once the test report is given to us we are legally secure to start selling the machine in Australia and New Zealand.

BACKGROUND INFORMATION:

Common-mode noise is the predominant cause of radiation produced by equipment such as the Mangrove. Common-mode noise is when the same (in-phase) signal is present on both the positive and negative terminals of a load. Differential-mode (or normal-mode) is the case when the noise on the positive and negative lines are are out-of-phase causing a difference in potential across the load. The suppression necessary for common-mode noise is the use of a low-pass filter or choke (series inductance) on every line that is susceptible.

By No machine-readable author provided. NekoJaNekoJa~commonswiki assumed (based on copyright claims). [GFDL (http://www.gnu.org/copyleft/fdl.html), CC-BY-SA-3.0 (http://creativecommons.org/licenses/by-sa/3.0/) or CC BY-SA 2.5-2.0-1.0 (http://creativecommons.org/licenses/by-sa/2.5-2.0-1.0)], via Wikimedia Commons
EQUIPMENT:

An HP 8566B Spectrum Analyzer was used when testing radiated emissions.

Here are images of the machine in the EMI chamber:
See EMI Test Lab LLC Report.

PROCEDURE:

EMI Testing Procedure:
Place the machine on the turning table in the EMI chamber. Power the machined with a 240VRMS (50Hz) source. Run through the spectrum (30MHz - 1GHz) with the antenna in its horizontal and vertical positions. If any frequency is above the specified limit then examine those frequencies individually and move and/or unplug wires to find the source.

Conducted Emissions Procedure:
Place the machine on a table with a specified distance away from the AC power source. Set the AC source to 240VRMS (50Hz). Perform average and quasi-peak measurements on both line and neutral.

TEST DATA and COMPLETE RESULTS:

The following data was gathered on 11/20/2015 when Juniperbush passed the requirements:

EMC Test Data:

Here is a table summarizing the frequencies closest to the limit:
Printing from SD:

Printing from laptop:

Any value on the Limit delta column greater than 0 dBμV/m would be considered failing the AS/NZ CISPR22:2010 Class A standard.
Conducted emissions test results (line):
See EMI Test Lab LLC Report.

Conducted emissions test results (neutral):
See EMI Test Lab LLC Report.
OTHER INFO:

The AS/NZ CISPR22:2010 Class A standard is a requirement to market and sell the machine in Australia and New Zealand. Once the data is collected that shows the machine passes the standard an RCM label must be applied to the machines that are solid in the targeted country and record-keeping requirements must also be fulfilled. The test that is conducted is almost identical to the FCC requirement except the applied AC source is 240VRMS @ 50Hz.

Taken from the ACMA EMC Booklet:
http://www.acma.gov.au/~/media/Technical%20Regulation%20Development/Publication/pdf/EMC_Booklet_pdf.pdf
[CC-BY © Commonwealth of Australia (Australian Communications and Media Authority) 2014.]

What are compliance levels?
The EMC Labelling Notice identifies three compliance levels. Each level specifies the evidence a supplier must obtain to demonstrate the compliance of devices to the applicable standard. The compliance level, in a given instance, relates to the risk associated with non-compliance with an applicable standard.

In simple terms, the higher the compliance level, the greater the risk presented by a non-compliant device. The greater the risk presented, the more comprehensive the record-keeping requirements.

There are three compliance levels:

1. Compliance level one (‘low-risk’ devices)
A compliance level one device (low-risk) is one that is neither a medium- nor a high-risk device.

2. Compliance level two (‘medium-risk’ devices)
A compliance level two device (medium-risk) is one that is not a high-risk device and contains one or more of the following:
a switch mode power supply
a transistor switching circuit
a microprocessor a commutator
a slip ring motor
an electronic device operating in a switching or non-linear mode.

A battery-powered device is not a medium-risk device unless the ACMA has declared it to be so. Note: Rectifier diodes are not considered to be electronic devices operating in a switching or non-linear mode for the purposes of the definition of a medium-risk device.

3. Compliance level three (‘high-risk’ devices)
A compliance level three device is a high-risk device; as a consequence, the required level of compliance documentation is higher.

A compliance level three device (high-risk) is one described as ‘Group 2 ISM equipment’ in AS/NZS CISPR 11:2004 (2nd edition). Examples of compliance level three devices include microwave ovens, induction cookers, RF welding machines, arc welding machines and electrodischarge machining (EDM) equipment.

What are the requirements of each compliance level?
Compliance level one
For compliance level one, a supplier is not required to hold a test report. However, as part of the compliance record the supplier must hold:
a description of the device
a Declaration of Conformity.
Note: Though low-risk devices only require a Declaration of Conformity, the supplier should still be confident that the device complies with the applicable standard. It is the supplier’s choice to maintain a test report supporting conformity. The penalty for supply of a non-standard device is not affected by its compliance level.

Compliance level two
For compliance level two, the supplier must hold as part of the compliance record:
- a description of the device
- a Declaration of Conformity
- either a test report from a testing body that confirms the device meets the requirements of the applicable standard (the report does not need to come from an accredited test laboratory) or
- a technical construction file stating the device would comply with the applicable standard

Note: For a definition of accredited testing laboratories, see Where can I have my device tested? below. if applicable, have explanatory documentation that specifies correct installation and operation procedures to minimise the possibility that a device will be installed or operated incorrectly.

The supplier accepts total responsibility for device conformity and needs to make a commercial decision on the level of testing required. When making the decision, the supplier should keep in mind the interference potential of the device.

Where a supplier chooses to use non-accredited testing, including in-house or self testing, to support their Declaration of Conformity, the ACMA reserves the right to ask for additional evidence of conformity, if considered necessary.

Compliance level three
For compliance level three, the supplier must hold as part of the compliance record:
a description of the device
a Declaration of Conformity
an accredited test report issued by an accredited testing body or
a technical construction file stating the device would comply with the applicable standard
if applicable, have explanatory documentation that specifies correct installation and operation procedures to minimise the possibility that a device will be installed or operated incorrectly.

Under compliance level three, the accredited test report must be produced by an accredited testing body for conformity with the applicable standard.

For information on interpretation of test results, refer to the EMC Labelling Notice.

The difference between compliance levels two and three is that all test reports for compliance level three must be accredited test reports obtained from an accredited testing body.
Where can I have my device tested?
Compliance level one and two devices may be assessed by a testing body, an accredited testing body or other suitable means.

Compliance level three requires applicable devices to be tested by a laboratory that is appropriately accredited for this purpose—an accredited testing body—or have a Technical Construction File (including a statement from a competent body). Compliance level three covers equipment from group two industrial, scientific and medical equipment, as per AS/NZS CISPR 11:2004 (2nd edition).

An accredited testing body is one that has been accredited by the National Association of Testing Authorities (NATA) or by a NATA mutual recognition agreement (MRA) partner.

There are a number of overseas laboratories that have been accredited through a MRA with NATA. Suppliers should contact NATA for current details of MRA partners or accredited testing bodies (see Contact details).

The ACMA suggests that the supplier checks the accreditation of the laboratory when arranging for the testing of a device, as not all laboratories hold accreditation for all standards. Although non-accredited reports may be acceptable for compliance level two devices, they do not hold the same level of authority as an accredited report.

The test report must show:
the tests conducted
the results of the tests, including test data
whether the results of the tests show that the device meets the applicable standard.

The supplier accepts total responsibility for device conformity and needs to make a commercial decision on the level of testing required. When making the decision, the supplier should keep in mind the interference potential of the device.

In all cases, the ACMA reserves the right to ask for more evidence of conformity, if considered necessary.

NATA has accredited a number of companies for various EMC standards. Contact details for the accredited testing bodies are available from the NATA website. The ACMA will use NATA-accredited testing as the benchmark.

Can I use an overseas test report?
A test report from an overseas test laboratory is acceptable where the device has been tested to the relevant applicable standard. The applicable standards are listed on the ACMA website.

Test reports from overseas laboratories must be written in English.

List of NATA accredited/ACMA recognized labs:
http://www.nata.com.au/nata/images/pdf_files/rtalist.pdf