Title: Z Min Switch/Auto Leveling
Test Plan: TP-RD-00006
Document Date: 10/6/15
Test Date: 10/06/15
Testing Location: R & D Lab

PURPOSE:

This test series is to verify and approve the life and functionality of the Z Min Switch and the auto leveling feature per design requirements indicated in the body of this test plan. Since the two may be testing congruently without impacting the results, they will be done together.

RESULTS SUMMARY:

Test 2: The printer successfully completed a print following 3 minutes of contact between the nozzle at 295C (it dropped to 282C following the contact with the switch). Teardown of the switch revealed no visible internal damage

CONCLUSION:

A pass on the z min switch is defined where the z min switch does not fail or create any subsequent issues within one year of use. The product Passes/does not pass the test as specified.

A pass for the auto bed leveling is defined as a successful first layer that measures between .3 and .45.

Recommendations are to ship the product as proposed.
Recommendations are to make the following improvements to the product and components:
Retesting of the product needs to occur/ retesting is not necessary/ retesting recommended if future modifications are made.

BACKGROUND INFORMATION:

The min switch is a new variety. It is a stainless steel push button. During testing, no damage that would impact the proper function of the switch should occur, was no info on life expectancy for this switch from manufacture.

History has shown that plastic build-up on the nozzle may cause auto bed leveling to fail and may destroy the bed. Having this work consistently is essential since there is not a built in fail safe for auto leveling.

The definition of a heavy user is approximately 700 prints in a year period.

The wipe sequence will be slower than the one on the mini since the tool head is being pushed in less stable position.

EQUIPMENT:

Taz printer with bed washers, a split z min, wiper pad, and momentary switch.

PROCEDURE:

Test 1: A cycling print should be set up asap to print small parts (>5min print) in cycles, ideally at least 25 to a bed. At 2 4-hour print cycles per day.
Test 2: To test a high heat failure mode of the printer, the hotend will be heated to 295C and homed onto the switch. After 3 minutes a print should be kicked off and complete sucessfully.

Test 3: To test the plastic buildup on nozzle failure mode, we will cause severe buildup of plastic on nozzle by driving hot nozzle into a pile of plastic and letting it cool. The printer should then be able to preform a successful home/wipe/probe/print sequence

TEST DATA and COMPLETE RESULTS:

Illustration 1: Tech drawing for switch