TAZ 1 (May 2013) to TAZ 2(Oct. 2013):

TL:DR: Adding an LCD screen and SD card reader make tetherless printing possible.

- The printed electronics box was replaced with a sheet metal version.
- An LCD screen and SD card reader were added for tetherless control and printing.
- The printed name plate and frame connectors were replaced with laser cut acrylic versions for increased frame rigidity.

TAZ 2(Oct. 2013) to TAZ 3(Dec. 2013):

TL:DR: A new heat-pad and 24V power supply make the heating of the build plate and nozzle much faster and more consistent.

- The 12V Power Supply from the TAZ 2 was replaced with a 24V unit for faster heating of the build plate.
- The heatpad for the build plate was replaced with a higher quality 24V unit for faster and more even heating.
- The spool holding mechanism was redesigned for much faster loading and unloading of filament.
- The Y axis was modified to be much more precise and easier to install.

TAZ 3(Dec. 2013) to TAZ 4(May 2014):

TL:DR: The z-axis was redesigned and a cooling fan added for much more accurate printing, as well as a more modular control box.

- The electronics case was reworked to be more modular and stable, as well as to make the addition of a dual extruder much easier.
- The X-axis ends were redesigned to be much stiffer
- The Z-axis screws were changed to high precision machined lead screws for greatly improved control over layer height and positioning.
- An extrusion fan (previously an accessory) was added to the toolhead as standard, allowing active cooling of the part as it's being printed.

TAZ 4(May 2014) to TAZ 5(Feb. 2015):
TL:DR: The TAZ 5 incorporated an improved hotend and bed surface from the Lulzbot Mini.

- The hotend was upgraded from the Budaschnozzle to the AO-Hexagon, an actively cooled all metal hotend based one the popular Hexagon hotend, increasing the maximum print temperature to 300C from 230C.
  - The modified version of the hotend features redundant heater retention for safety and a longer melt zone for smoother high speed printing than other hotends on the market.
  - The TAZ 5 initially shipped with an 0.35mm nozzle but that was increased mid run to 0.5mm to decrease print times.
- The PET bed covering was replaced with PEI, making it possible to print in most materials with no glue or acetone slurry application.
- The 24V power supply was upgraded form 360W to a 400W unit for faster and more consistent heating.

TAZ 5(Feb. 2015) to TAZ 6(Q1-2 2016):

TL;DR: Every part of the TAZ 5 was redrawn and reworked. The machine is more precise, more reliable and incorporates an advanced version Mini's autoleveling for plug and play printing.

- Full freecad redraw – every part of the printer was redrawn in FreeCAD, making this the most open source printer we (or anyone) have ever made. This also expands the user's ability to explore and modify their printer.
- Updated toolhead
  - Stiffer design for higher precision prints
  - Support for auto leveling
  - Heatsink fan upgraded to allow even greater versatility in materials
  - Bi-directional fans – ensures that all sides of a printed part get enough cooling
  - Pelonis fan upgrade allows mush finer control over fan speed and the ability to cool with much more air than previous toolheads
- X-Axis smooth rods increased from 10mm OD to 12mm OD to decrease “droop” in the x-axis to >0.020mm
- All Igus bushings changed to precision grade for higher accuracy
- Next generation auto leveling added with detection for wipe malfunction detection, making the TAZ6 as easy to set up as the LulzBot Mini
  - Ultra fine Z offset adjustment is now possible through the LCD
- Frame is now reinforced with aluminum brackets for increased stiffness
- Max endstops added to prevent accidental axis overrun
- Z-axis redesigned to allow for smooth precise motion with no need for grease. Incorporated Ninjaflex gaskets to prevent binding.
- Packaging redesigned from the ground up, it's now both recycled and recyclable
- Fully integrated electronics package contains all electronics necessary to run a printer and eliminates risk of failure from electric shock. All harnesses are labeled for easy
- Over 120 reworked print profiles available out of the box
- All steppers changed out for higher quality Moon's steppers
- FCC Class B and CE Certified
- Z axis rods moved rearward for higher stiffness and better weight distribution
- Firmware based on the latest stable release of marlin – incorporating all of the latest advancements from the open source printing community
  - Our improvements include:
    - Higher communication rate
    - Improved thermal runaway protection
    - Switch debounce to eliminate false endstop triggers
    - Layer tracking