Install guide for TAZ two-piece bed

1.)You just upgraded your LulzBot desktop 3D printer with the two-piece bed. After following this quick start guide, your lulzbot TAZ 3D printer will be more capable then ever. Let’s get started!

2.)Included materials:
TAZ PEI Modular Print Surface(KT-HB0012), TAZ Heat Bed: 14-3/4 x 14-3/4 x 1/2 44 ECT B Brown Die Cut One Piece Folder(SH-BX0075), TAZ Heat Bed: 18 x 18 Die Cut Pad (insert) (SH-PA0048), 16 x 16" 6 Mil Reclosable Bags, (SH-BA0008), TAZ PEI Modular Print Surface (AS-HB0003), Disposable Desiccant Bag, Silica Gel, for 24 Cubic Inches(SH-PG0099)

TAZ Modular Heated Print Bed(KT-HB0013), TAZ Heater Assem from TEMPCO 360 Watt 24V with felt(AS-HE0004), Tubing Corrugated Loom .25”, Black, 3200’ Box(EL-MS0073), Wire Tie, 8” Black, pk 1000, (HD-MS0058), TAZ Heat Bed: 14-3/4 x 14-3/4 x 1/2 44 ECT B Brown Die Cut One Piece Folder(SH-BX0075), TAZ Heat Bed: 18 x 18 Die Cut Pad (insert)(SH-PA0048)

3.) Items required: Metric hex drivers 2MM, LulzBot TAZ 6, TAZ PEI Modular Print Surface(KT-HB0012), TAZ Modular Heated Print Bed(KT-HB0013)

4.)Raise Zaxis to shipping position

5.)Turn off your Lulzbot TAZ 6 3D Printer

6.)Unclip heatbed heater and thermistor wires(White and red) from heatbed harness(Purple and yellow), and disconnect 8-pin connector.

7.)Using your 2MM hex driver, remove the screws and washers. Then set hardware aside for future use to secure your new heat bed.

8.)Proceed to remove old bed and discard properly.

9.)Open box TAZ Modular Heated Print Bed(KT-HB0013), be careful if using a knife as blade may damage contents.

10.)Place Modular Heated Print Bed on TAZ 6 bed plate

11.)Open box TAZ PEI Modular Print Surface(KT-HB0012) and place onto the TAZ Modular Heated Print Bed(KT-HB0013).

12.) place washer with screw into 8MM spacer and torque to 5inLB.

13.) Plug in heatbed heater and thermistor wires(White and red) from heatbed harness(Purple and yellow), and connect 8-pin connector.

14.) Install complete!