Model:	TAZ 6.0 3D Printer
  Serial Number:	_______________________
  Heat Bed Batch#:	_______________________
  Date Completed:	_______________________
  Completed by:	_______________________

Configuration:
Electronics:	RAMBo 1.3L
Firmware:	Marlin 2016-Q1
Nozzle:	Hexagon Hotend, LulzBot Edition with 0.50mm nozzle
Settings:
Part	steps/mm	max length	microstep mode	digipot
X Motor	100.5	298	16	175
Y Motor	100.5	275	16	175
Z Motor	1600	250	16	240
E0 Motor		NA	16	135

    Z Offset: _______________________

General
- Are all the screws and zip ties tight?
- Are the X and Y axis square to each other?
- Are the gaps at the ends of the extrusion closed?
- Are all the parts flush and straight to the edges with clean lines?
- Is the t-nut for the 2nd extruder installed correctly?
- Does the SD card slide in and out of the slot freely?
- Has the protective plastic been removed from the LCD and LCD cover?
- Are the current version of parts being used?
- Verify that the following are mounted correctly:
    1. Feed tube, tube on back side of mount
    2. Spool Arm, correct height
    3. Finger clip, taller side on left
- Are the switches tight? They shouldn't wiggle side to side.
- Are all 11 rubber feet installed?
- Is the PEI tape free of bubbles and wrinkles?
- Is the heat bed adhesive smooth and consistent?
- Does filament slide through the feed tube?
Y Axis
- Does the Y bed move freely back and forth?
- Is the Y bed tight side to side from motion and twisting?
- Are all the screws on the bearing holders tight?
- Does the Y belt rub the bottom of the y-idler by the bearings?
- Is the Y pulley tight?
- Is one of the set screws on the Y pulley aligned with the flat on the motor shaft?
- Are both pulley set screws tightened?
- Has loctite been applied to the set screws?
- Is the level of the Y pulley at the same height as where the belt mounts on the belt holder?
- Is the Y belt tight?
- Are all the Y mounting brackets flush and tight?
- Are the belts trimmed far enough to not interfere with the pulley or bearing?
- Are the plastic parts flush to the top of the y end plate?

X Axis
- Is the X pulley tight?
- Is one of the set screws on the X pulley aligned with the flat on the motor shaft?
- Are both pulley set screws tightened?
- Has loctite been applied to the set screws?
- Is the belt free from rubbing anywhere during motion?
- Is the X belt tight?
- Does the X axis move freely end to end?
- Are the X bars flush with the outside for the X-end idler (right side)?
- Are the set screws that hold the X bars tight?
- Are the belts trimmed far enough to not interfere with the pulley or bearing?
- Is the x-axis level and parallel to the bed?

Z Axis
- Do the Z drive rods rotate smoothly with no up and down movement between the bearings?
- Are the four Z coupler set screws tight and aligned with flats on the drive rods and motors?
- Has loctite been applied to the set screws?
- Are the Z smooth rods flush with the top plate?

Extruder
- Can you adjust the extruder springs?
- Are the V grooves on the extruder gears lined up?
- Is the extruder mount secure on the X carriage?
- Are the extrusion fans mounted correctly?
- Is the heatsink fan mounted correctly?
- Does the idler bearing stick out of the idler block?
- Is the hobbing aligned to the hole in the extruder?
- Is the set screw in the small gear tight and on the flat of the motor shaft?
- Can you feed filament about 100mm from the top of the extruder?
- Are the gears tight with no back-lash?
- Do the extruder gears turn smoothly for several rotations?

Electronics
- Are the screws that fasten the control box to the frame tight?
- Can you plug in USB cable from the outside of the enclosure?
- Is the plug cover for second extruder installed with the strap attached to the lower right screw?
- Is the LCD secured in place firmly?
- Is the LCD knob tightly secured to the LCD?

Test and Verification Results:
- LCD functions normally.
- Belts aligned on bearings and properly tensioned.
- Verify case fan is spinning freely.
- Verify the heatsink fan is running.
- Verify you can run the extrusion fans.
- Hexagon Hotend temperature control verified.
- Extruder calibration verified. Check that eeprom values are correct.
- Z offset calibrated and verified.
- Bed level consistent across bed.
- X, Y and Z stop switches verified.
- Flat of the nozzle contacts all 4 bed corners.
- Wipe sequence is in center of wiper pad
- Bed temperature control verified.
- Cables secure and free of interference/contact with table motion.
- Cable connectors fully engaged and oriented correctly.
- Bearing conditioning (burnin) complete.
- X, Y and Z motion smooth over range and speeds.
- Test print (Octopus) successful.
- Loctite applied to all pulley and coupler set screws.