Athena engineering validation testing (EVT) phase

4 machines
- Brent
- Ben
- Joe
- Patrick / Eric
Features
- 15mm profile rail on all axes
- Z-belt drive w/ gear reduced NEMA 17’s
  - likely 27:1 gearboxes to prevent back drive
- Likely TAZ tower of power based
  - May add replicate to TOP, custom board as it’s developed
  - Will use TAZ PSU for now
- Will use TAZ 2 piece bed setup
  - Heat spreader will be 1/4” mic6
  - working on easy remove bed corners
- Enclosed
  - Currently acrylic and sheet metal
    - ESD acrylic?
  - Depending on how well it seals we may need cooling for hotend, motors, electronics, part
Undecided features (will be developed in parallel until a decision is made)
- toolhead switching or dual independent or dual toolhead
- Electronics embedded or Electronics in separate side case
- Patstruder or e3d aero or Bondtech (pending openness) or ???
- Strut frame or sheet metal frame
- belt or multistart screw

Toolhead ecosystem:

Features:
- BRAINS on all toolheads
  - onboard storage of esteps
  - stored xy offset?
  - Stored statistics? (run time for maintenance / replacement)
- fastenerless and connectorless attachment
- kinematic coupling for location
Toolhead options:
- 0.25 v6
- 0.4/0.5 vs/AO3D
- 0.8 volcano
- 1.2 MOAR
- Flexy
  - 0.6
  - 1.0/1.2
- High temp?
  - Size?
  - 400? 500?
- Hardened (for abrasive)?
  - size? (avoid small sizes for more strength and fewer clogs)
- Dual? (see above)