GENERAL DESCRIPTION:

FEATURES:

- Unique and Distinctive Industrial Design
- UL enclosure
- Out of box dual printing
- True Bed Leveling
- Unique tool head switching
- Simple XY with belt driven Z axis
- Full color touch screen interface
- Consumable/replaceable heated print surface
- Wireless Capability
- Modified E3d hot end
- Electronics with on board Linux
- Software – Cura2
- FSF RYF, OSHW Certification

SPECIFICATIONS:

Description	Specification

Layer Height	.05mm-.50mm with 2 head mix
Minimum recommended feature size	mm (0.5 nozzle) / mm (1.2 nozzle)
Nozzle Size	.5mm – Default (for both) / 1.2mm – Yes / .25mm – Yes / .80mm – Optional
Feed Rates	? measurement ?
Filament Size	3mm
Bed Heating Max Temp	110°C
Bed heat up time
Operating Temperature Range	0°C – 50 °C
Print Volume	300 X 300 X 300
Drop Testing
Acoustic Levels	Xxx.xx Db
Product Dimensions
Operating Keep out area
Weight
Certifications	UL, FCC Class B, CE, Weee, CSA
Maximum Carriage Speed	mm/s
Carriage Positioning Resolution	mm
Thermal Load	BTU/hr or watts