Copyright 2017, Aleph Objects, Inc. CC-BY-SA 4.0

Athena Design Handoff Document

Table Of Contents:
1. Introduction
2. Overview
  1. General
  2. Motion
  3. Structure
  4. Assembly
3. Part status and details
  1. Left / Right side assembly
  2. Rear Panel
  3. Bed assembly
  4. X axis
  5. Filament / UI case
  6. Front Door
  7. Lid
  8. Packaging

1.0 Introduction:
The purpose of this document is to lay out the current design status as well as the tasks that will need to be completed in order to bring the printer to market. As of June 2017 the printer is in early engineering evaluation stage.

2.1: General Summary:
The goal of the athena printer development is to add a 3rd printer to the LulzBot lineup, one that is enclosed, teatherless and capable of reliable dual extrusion. Below are the design specifications that were developed for the athena project by the new product introduction team.

	First Release	Notes
Industrial Design	More professional / Minimal printed parts / No printed parts - Stretch
Build Volume	300mm x 300mm x 300mm	280 x 280 x 280 effective BV unless we go away from using TAZ bed
Bed	Consumable bed/print surface / Heated / Easily removable/replaceable (modular)
Tool head Standard	Out of box dual Printing
Tool Head Add On	On-board logic (self-identification)
Tool Head Mechanics	Tool Changing – Self-changing as stretch goal / Direct Drive
Hot End	Modified E3D / Flexible-capable – Stretch / High Temp (to 500C) - Stretch
Enclosed	Good visibility / Heat retention to 50C / LED Lights - Stretch
Communication Options	Tethered/PC/Ethernet/USB Serial – Yes / USB Thumb Drive – Yes / WiFi Capable– Yes (with after-market dongle) / WiFi Standard – Stretch goal / Standard SD or Micro SD – No
Motion System	Simple XY with belt-driven Z-axis / True auto bed leveling / Automated xy calibration
Accessories	Camera – Super Stretch / Storage Pedestal –Super Stretch / UPS Pedestal – Super Stretch / Humidity Control Pedestal – Super Stretch
New Electronics Board (Cimarron)	On-board Linux / Extra pins / Extra drivers
Software	Cura 2 / Octoprint – Stretch goal / Cluster management – Super stretch goal
Layer Height	.05mm-.50mm with 2 head mix
Nozzle Size	.5mm – Default (for both) / 1.2mm – Yes / .25mm – Yes / .80mm – Optional
Filament Size	3mm – Yes / 1.75mm compatible – Stretch goal for PLA, ABS
Retail Price	$4,000-$5000 (USD)
Gross Margin	$2,680-$3,350 (66.25%)
Cost	$1,350-$1,700 (33.75%)	BOM + Labor
BOM Est.	$1,200-$1,500 (30.00%)	Room for 2-4% higher BOM
Labor Est.	$150-$200 (03.75%)	Consider together with BOM
On-Board Software (formerly firmware)	On-board GNU/Linux / Filament misfeed detection – Stretch / On-Board Slicing – Super Stretch
Display/Controls	Full Color – Min. 2 in. x 3 in. / Control knob/button / Touch Screen - Stretch
Regulatory	UL, FCC Class B, CE, Weee, CSA
User Freedom	FSF RYF, OSHW Certification, No patents
Packaging	Ships in not white box / Easy to remove and repack

2.2: Motion System Summary

The motion system of the Athena printer is set up as what we’re calling a simple YX, where the toolhead moves back and forth along the x axis, which is itself moved forward and backwards along the y axis. This system was chosen for it’s robustness, modularity and self aligning nature. More information on this system is available in the animas project repository.

Above: Simple XY motion system

Below the xy gantry, the bed drops in Z. The current design uses 15mm wide profile rails in all 3 axes, driven by bipolar steppers using GT2 belts. The z is positioned by 3 separately controlled gear reduced stepper motors, enabling true bed leveling which eliminates the problems associated with tramming style “auto-leveling”. The use of belts vs leadscrews in z should eliminate some of the main causes of z-banding while greatly reducing the cost and increase in weight associated with stretching the printer along the z axis.

Above: Render of the Z axis hardware

The barrel style belt clamps used in the current generation prototypes seem to be working well, and may do away with many of the overtightening and cracking issues that we’ve had with belt mounts so far. The looped sections should probably be widened to match the minimum bend radius of the belt.

Above: Barrel style clamp from the x motor mount (GT2 belt version). Note that this version has not yet been modified to accommodate the minimum bend radius of the belt.

2.3: Printer Structure Summary

The structure of the printer consists of 5 main sub assemblies; the left and right panels, rear panel, Z-platform assembly and the side case assembly. The motion system is mounted to aluminum extrusion bolted to polycarbonate panels that make up the left and right assemblies. Using the polycarbonate panels as a structural component rather than a removable covering should help to reduce weight , cost and part count. The PC panels as a structural member also add a small amount of compliance which should help the printer maintain squareness during shipping.

Above: right side panel

The left and right side assemblies are designed so that the aluminum extrusion pieces can be held in place from below by a clamping jig while the polycarbonate panel is bolted down from above, which will ensure perpendicularity of the y and z axes without requiring tight tolerances in either the aluminum extrusion or the polycarbonate panels. The rear panel subassembly consists of a sheet metal plate that mounts the electronics enclosure and the toolhead docks, and joins together the left and right side panels. The electronics enclosure will be designed as a simple 5 sided sheet metal box deep enough to fit the power supply that bolts to the outside of the printer. The electronics will be accessible through an access panel on the rear side of the printer (either hinged and latched or screwed in place).

The front and rear lower beams are structural and will extend from the printer box structure underneath the filament / UI case. This is intended to allow users to lift the machine from underneath on the left and right hand sides, encouraging a team lift (the printer will likely weigh ~100lb). There will need to be a cross member in the lower right edge of the filament case bolted to the lower beams in order to brace the filament case for lifting. It would also be better to have a bit of a radius or a handle on that lower edge to make lifting the printer comfortable.

2.4: Printer Assembly Summary

Currently, the printer assembly will be broken down into 5 main subassemblies, and will be manufactured at around 6 different assembly stations.
Left / Right side panels: these will be built up on custom assembly jigs at dedicated assembly stations. These jigs should be designed to be removed from the work station so that the line can transition quickly between making athena left panels, right panels or TAZ frames.

Above: Simple fixture for assembly of the right side panel.

Whole frame assembly
The goal of the whole frame assembly is to hold the left and right side panels in place and parallel to each other while the bottom and back plates are bolted in place. This should ensure that the final machine will have very little skew in any of the x, y or z axes.

It would be ideal if the fixture actually referenced the linear rails directly (rubber coated magnets?) in order to avoid having too many parts in the stackup. It will be important to avoid damaging the bearing surfaces of the profile rails.

The best way to build this fixture will probably be to start with a portable welding / layup cart such as the rino cart from stronghand tools, then build up custom mounts that can be easily calibrated. I expect the design of this fixture to be one of the most important factors in being able to produce high quality machines quickly.

Infrastructure
As the full printer assembly will be well beyond the OSHA recommended lifting weight for 1 person (50lbs), it will be important to implement some sort of printer lift in assembly, or to structure the assembly tasks into 2 person teams who can move the printer toghether, likely starting as the printer frame is being removed from the whole frame fixture.

3.1: Subassembly breakdown and status

Left and right side panels:
These are grouped together because the assembly and part-list are very similar. The z motor mount and idler are currently working well and likely don’t need much work. The idler pulley kit is working very well. The 3/16” polycarbonate panels used on the first prototype batch are the thickest size that can be stamped; if they perform well we should stay with that size in order to keep cost and weight low. The panels that came in seem to scratch easily, it would be a good idea to keep the protective film on for as long as possible in the assembly process, or to look into scratch resistant versions of PC. The aluminum extrusion endoskeleton design does a good job of creating a stiff and square frame, but getting the t-nuts in place is tedious and not something we’ll want to do in assembly. For the production version we should use a cleaner looking extrusion like the 40-4020 and have either the manufacturer or a machine shop (quattro?) drill and tap the M5 panel mounting holes in the clean side of the extrusion to eliminate the need for t-nuts. This is something that could likely be sourced through futura industries.

Above: drilled and tapped aluminum extrusion for panel mount points

For mounting of the profile rails to the inside of the extrusion, I would use machined acetal jigs to center the rails on the extrusion along with a custom t-nut bar to aid in alignment. On the right side of the printer the front rail should be set parallel to the extrusion using the printed jig, while the rear rail should be located using a bracket bolted to the front rail. This will ensure the 2 are parallel and the correct distance apart.

Above: nutrail for easily securing profile rail

The Y motor mount and idler are currently working well as well, but may need to be redesigned to be machined brackets. The mounting extrusion for the y axis profile rails will still need to be 20x20mm extrusion in order to mount the z-motor-mount under the rail, but the version with the clean outer facing surface should be used.

3.2: Rear Panel
The rear panel should be a fairly simple sheet metal assembly with the exception of the toolhead mounts. The actual electronics box should be designed as a simple sheet metal box deep enough to house the largest component, presumably the power supply. Once the full electronics package is designed it should be pretty simple to design the box around it. Pay extra attention to the surfaces that need to be masked, this gets surprisingly expensive if it isn’t simple. It helps reduce cost a lot if you stick with standard widths of masking tape (this is generally what they use).

Also keep in mind that the sheet metal of the outer back panel shouldn’t set the distance between the left and right sides of the printer, the jig used to hold the right and left panels parallel (whole-frame fixture) should do this. Allow oversized holes in the sheet metal to accomplish this, along with making sure that the upper piece of aluminum extrusion is slightly undersized or mounted in a way that allows an bit of adjustment.

The whole frame fixture will need to be designed as a fixture that mounts the left and right panels upside down so that the rear panel and the bottom panel can be installed with the frame on the whole frame fixture. This would be accomplished best by using an off the shelf welding fixturing table with magnetic mounting points that locate the sides by referencing the profile rail directly.

3.2: Bed Assembly

The bed assembly will consist of 3 main components; the z-plate, heater assembly and build surface. It’s very similar to the TAZ 6 modular bed system and will likely use the same build surfaces. The current bed design will need to be shortened in the x axis along with the top and bottom panels once the needed travel for the x axis is defined.

The belt loops currently in the model interfere with the z motor and idler, they should be redesigned so that the belt loop and barrel both end before the top and bottom surfaces of the flange.

The bed plate is currently designed to make it easy to slide the print surface on and off by bending a lead in flange on the front of the heat spreader as well as chamfering the lower edge of the bed leveling washers. There will need to be some sort of guide to allow the bed to slide easily in and out while being rigidly held in place, and rounding the corners of the bed surface (likely glass) will go a long way toward making the process efficient. If movement of the bed plate is an issue, it should be fairly easy to add in a sprung latch to lock the bed in place when it’s slid all the way into place.

Above: detail view of the slide in bed assembly.

3.4: X Assembly
The x assembly as it’s currently designed consists of a single piece of extrusion bolted to the carriages on the y axis. The current design uses printed mounts to couple to the profile carriages, but these should be machined components for production as these brackets set the perpendicularity of the x axis to the y axis. The x rail, x-motor mount and x-idler all bolt to this extrusion. Currently, the assembly was designed for a toolhead with it’s nozzle much closer to the x axis so it will likely need to be modified to match the new toolhead depth.

3.5: Filament and user interface case
The filament case is a sheet metal enclosure that also houses the human machine interface. The current design is in blender as it was easier to make quick changes for industrial design concept rendering. I would recommend getting in touch with a sheet metal vendor to talk over the most cost effective way to build the current shape before remodeling in freecad. Keep in mind that the filament case will need to be braced along the lower right edge

3.5/6: Front Door / Top panel
The front door and top panel will need to be made out of a thicker material than the polycarbonate used on the side panels; something around 1/4”-3/8” should work well. It would be best if we could create a seal between the frame of the door and the top panel in order to retain heat better, although this isn’t a requirement for athena.

3.7: Packaging

The full printer assembly is likely going to weigh upwards of 100lbs, and closer to ~120-150 for a version scaled in z. Because of this, we’ll likely need to ship the printer either in a crate or a reinforced box, which is pretty consistent with similarly sized printers already on the market.

It would be best if the printer could be transported from final assembly to the packaging area via a conveyor in order to eliminate the need for overhead crane or team lifting of the units. For the same reason, it would be best if the bulk of the packaging could be lifted off of the printer, rather than the printer being lifted out of the packaging.

Tasklist:
  - Highest priority:
    - EPM Development
    - Design LR side assembly fixtures
      - This is super critical in order to make sure that these machines can be produced quickly and precisely.
      - Recommend 2 parallel paths
        - Low risk: oversized channels milled in aluminum to locate extrusion. Develop this in order to make late stage prototypes and possibly early production batches.
        - High risk: Mechanical / pneumatic kinetic fixture. A kinematic fixture would be able to produce more accurate machines but is significantly more complex than the simple milled fixture. This should be developed, but shouldn’t necessarily hold up the release of the printer
    - Design whole frame fixture
      - Use profile rails to locate LR panels, fixture holds while securing rear and bottom panels
      - Look into rhino cart welding rigs for these fixtures, it will be important to produce at least 1 more cart than is needed in order to keep the
  - Medium Priority:
    - Redesign X axis to fit new toolhead
      - The new toolhead is significantly farther forward than the previous version, because of this, the x-axis extrusion mounts should be moved to the rail side of the extrusion in order to allow the toolhead to access more of the bed plate
      - The waterjetted plates that make up the base of the x-motor mount and x-idler will need to be shrunk to get the belt bath as close to the moving center of mass as possible.
    - Design new bed plate assembly
    - Design electronics enclosure when layout is established
    - Begin to vet printed part gcode for strength & aesthetics
  - Low Priority:
    - Get test silkscreen samples
      - This will include PC panels, the stainless steel heat spreader plate as well as the z-plate and any other sheet metal parts. Laser etching should NOT be used on this printer.
    - Design / spec / source aesthetic extrusion
      - I have been basing a lot of the industrial design on using stock extrusion from 80/20, but futura industries would be another good source.
      - We need to find at minimum a 40mm 45deg chamfer style extrusion and a 20x20mm extrusion with 1 clean (unslotted) face.
    - Discuss drilling / tapping aluminum extrusion w/ vendor
    - If time allows, look into alternate x-axis belt path that gets the belt path closer to the moving center of mass.
      - In the extrusion???
    - Begin to build up rough OHAI kits for assembly