LulzBot Filament Testing Report

Manufacturer: Formfutura
Filament Type: LimoSolve HIPS
Tested By:
Date:

Ease of use:	X/10
Appearance:	X/10
Color consistency:	X/10
Print temperature Range (C):	(XXX-XXX/XX-XXX)
Variance in diameter: (x.xx-x.xx)
Minimum bend radius:
Prints using current Lulzbot profiles/temps:

General Notes:	(Be as detailed as possible)
- Decomposition above 300ºC. Do not print above this temperature
- Per Manufacturer:
  Melting point 105-140°C
  Decomposition temperature - >300°C

Recommended Print Profiles: (ie. should we include high clarity, high strength, etc.)

Heath or Environmental:

Decomposition Materials include: Carbon monoxide (CO), carbon dioxide (CO 2 ), tetrahydrofuran, low molecular weight oligomers, and other gaseous products of degradation can be given off if the
product is greatly overheated.

Disposal Options:
Dispose of material waste and residues in accordance with local regulations.

Recommendation:	(As thorough as possible)

Revision History

Revision Date	Modifications or Additions	Updated By
06.28.17	Document Created	J. Pettit