Agenda
pcDuino / Easy TAZ Mini
6/16/2014

- Scheduling
  ==========

  Regarding our production schedules, we will need two things:

  1) A production schedule from you that will outline week-by-week the process from now until final product is in hand with commitment dates for project milestones.  We will need this in order to coordinate integration and testing.

  2) A weekly status meeting.  We would like an in person meeting on Mondays at 10:30 AM.  If there is no one to meet in person due to travel, we would need a phone call.
- Engineering Specifications
  ==========================

  I have made some modifications to the list below.  Those changed or added are marked with an *.

  Core Board/Base Board:

  1. WiFi - requires a chipset with open source firmware

  *2. 2 USB host ports - We would like the option of using header pins to reduce cost/bulk of connectors.  (We were previously assuming a USB port would be needed for the touch screen)

  *3. 2GB NAND -- This is not required if cannot open source writing.  SD will be used instead. (We would be interested in eMMC)

  *4. LVDS touch screen LCD display (see below)

  5. A20

  *6. Audio in and out - Ability to connect a small speaker directly into the board and have amplified audio.

  7. Ethernet

  8. MIPI camera connector

  9. MicroSD card slot

  10. 10 GPIOs ( the arduino layout is not needed)

  11. headers for power in

  12. NO HDMI

  13. NO SATA

  14. NO battery

  15. NO infrared

  *16. Onboard circuitry allowing us to power the Core Board with 24V.

  *17. Onboard 24V RGB LED strip driver - Essentially, we'll need 3 GPIO with PWM capability to control MOSFETs outputting a 24V signal.

  LCD:

  The bezel on your current screen will not work for our design.  What we need is the bare metal form factor without the bezel.

  What we want is a 7-inch touch screen, much like the one in the HDMI kit, that connects to the Base Board directly.