Gladiola Feature Change/Addition	Notes
Cork/or other Dampening (z and y motors)	Using Moon’s dampener for Y axis, still reviewing for Z.
Wipe Fail Detect	Completed and need further testing
Thermal Runaway	Completed and need further testing
Moons Motors	Built up and testing with motors. Motors on BOM
Add fan guard inside of case on back side of fan to protect wiring captures and external ingress ease	Existing part – adding to BOM
Cable Chain Modifications/wiring improvements / - Add ferrules to all power carrying wires and all wires connected to screw terminals. / - Widen e-chains to maximum width available same height and radius in place today / - Change all wires in cable chains to wiring rated for continuous bend applications / - Correct wiring layout inside of the control box to address excessive wire bends, spiraling of wires, no service loops	Design Review held, prints out for quote and prototype
Sheet Metal / - Power entry module opening need to account for powder coat thickness and over / spray in the region. / - Bed Plate – modified outline to accommodate safety warning etching, modified for cable chain attachment and powder coating / - Bottom chassis – modified to accommodate cable chain attachment	Completed and out for quoting/prototyping
Pelonis Fans, extruder and case fan	So far current low speed fan is looking good. Testing thermal performance of z chip to verify
Tool head Mods	Decision not to move forward with most mods. Will be modifying the cap piece though
Plastic Components that are being modified or considering modified: / Belt Mount strengthened / Bearing holders on bed to add strain relief / Bed corners to match taz 6 and possibly other materials / Spool Mount - Spool mount v1.3, Mini- 50 NC's- propose extending mount tip 5mm to / improve fit up clearance. / Upper and lower chassis strain relief / X end motor / Possibly lower z’s if we do dampeners / Extruder body and toolhead brace if toolhead / Upper x bearing holder / Wiper mount to TAZ6 version	dafsdfds
Evaluate Alternative Materials for components	PCTPE Gears, Cheetah Handle(possibly)
PP-GP0175 Y Idler mount, v1.3, Mini- RMA's and production parts show split / parts, Change M8 FHS to a M8 BHCS, change screw head recess to accept the / BHCS
Hardware: / Black Oxide hardware- lacking oil protection- suggest dry finish / Propose increasing the screw length used to secure PP-GP0173 to PP-GP0171 as it only gives 1 to 2 threads engagement	Evaluating Options
Remove or actually use the Z axis over travel switch	Removing